## Slide 1: Sparky the Robotic Dog By: Mike Gerhard
IMDL Fall 99
Dr. A.A. Arroyo

## Slide 2: Sparky the Robotic Dog By: Mike Gerhard
Why a robotic dog?
Why this design?
Design goals
Tech Specs
The gait
Behaviors

## Slide 3: Why this design?
The choices in the robotic dog market are limited
All of the robotic dogs that I have seen in my research have been either too expensive and complicated for realistic purposes or very basic walk forward toys
Examples

## Slide 4: Why this design?
$$$
Simplicity
Ease of programming
Expandable platform

## Slide 5: The Expensive Alternative
AIBO by Sony
This robot can do everything that a real dog can and more
It should at a price tag of $2500
VERY limited release

## Slide 6: The Inexpensive Alternative

## Slide 7: The most common robotic platform
Uses at least 8 servos
This design called Bob by Steve Stancliff based on the the Thing platform uses 12 Servos

## Slide 8: Problems with the most common robotic platform
Too many servos
Too many batteries
very complicated movements
very complicated programming
$$$

## Slide 9: Advantages of my platform
$$$ -- relatively inexpensive at ~$100
Simple movements = simple programming
Adaptable -- boxy shape is good for adding stuff i.e. camera, sensors, arms, head, etc…
Turns on it’s own axis

## Slide 10: Disadvantages of my Design
Slow
Can’t step over things

## Slide 11: Design Goals
Walk Forward, Backward, Left and Right
Use only 4 -- 42oz/in servos
Avoid obstacles
Respond to voice commands
  the only one that I didn’t meet due to an unfortunate accident with a rather pricey voice module

## Slide 12: Tech Specs
Mekatronix TJPRO motherboard with a Motorola 68HC11A1 in expanded mode with 32kB RAM
4 -- 42 oz/in servos by Diamond hacked into PWM controlled gearhead motors
2 -- Sharp IR receivers hacked for an analog output with two IR LED’s for obstacle avoidance
4 -- Radio Shack IR emitter/detector pairs used as motor feedback for leg synchronization

## Slide 13: Emitter/detector pair schematic
#276-142 Radio Shack emitter/detector pair shown in red

## Slide 14: The Gait
Sparky walks by moving opposing pairs of legs.
Each pair is synchronized using the IR emitter/detector pairs for once per cycle synchronization

## Slide 15: Behaviors
Walks forward and backward
Turns left and right
Avoids obstacles
gets “scared” when the reprimand transmitter is used
Dances