## Slide 1: Towing Robot (Towbot)
Imdl (eel 4665c)
Instructors: Dr. a. Arroyo, dr. e. Schwartz, Dr. a. gray
Presented by diego de la hoz
On 28 January 2016
Notes: Automation has become a modern engineering interest. From simple excel spreadsheet calculations to industrial automated assembly lines. Automation, in many ways, has improved our ways of life in safety, speed, and efficiency
The idea of reaching an automated world intrigues all human minds.

## Slide 2: PROJECT OVERVIEW
Problem: In the real world, cars can be both a gain and a pain
  Car failure, Car accidents, Car needing transportation
  Challenges: Communication failure, Time delays, Unavailability
  Inefficient
Proposed Solution: Autonomous Towing Robots
  Their purpose is to autonomously locate and aid cars that need towing
Gain:
  On a large scale, create an automated towing robots network that would aid broken cars as needed.
  On a small scale, design a communication system between robots.
Notes: Any situation were the car is not able to move.
  If the car needs aid towing,
  Car is in poor network area
  Towing trucks are unavailable
  How so? In the next slides

## Slide 3: Behaviors
Robot A (Broken-down robot)
  Able to move and avoid obstacles through an environment
  Able to send a signal to Robot B (Towing robot) when it needs towing
  Future: Able to receive a signal from Robot B when it arrives to towing dock
Robot B (Towing robot)
  Able to identify the position, receive the pixel location from the god-camera
  Able to move and avoid obstacle through an environment
  Able to ‘tow’, attached to Robot A in order to tow to desired location
Future: Able to find the best path/ route to reach Robot A based on object recognition from the god-camera

## Slide 4: HARDWARE & SOFTWARE
Micro Metal Gearmotor (x2)
  298:1, 70 oz-in, 6 V
Encoder Gearmotor (x2)
  34:1, 130 oz-in, 6 V
Dual Motor Controller (x3)
  1.2 A, 4.5-15 V
  1 A, 4.5-13.5 V (x2)
Magnetic Encoder Pair
  12 CPR, 2.7-18 V
Pololu Wheel 40 x 7 mm Pair (x2)
PlayStation Eye Camera (x2)
Ultrasonic Module (x10)
Teensy 3.2
  32 bit processor at 72 MHz
  34 I/O pins, 256 KB of memory
Raspberry PI 2
  Quad-core at 900 MHz
  40 GPIO pins, 8 GB Micro SD

## Slide 5: CONCLUSION
Design two autonomous robots with different goals
Important factors that will need time and energy:
  Imagine Processing
  Coordinate transformation
  Latching mechanism
  Future: A Star- routing tool

## Slide 6: FUTURE WORK
Extensive research needs to be done in the following areas:
  Coordinate transformation
  Possibly A Star
Project is divided into two phases:
  Phase I: Obstacle avoidance, motor control
  Phase II: Image processing, communication