## Slide 1: The Frodo
EEL-5666 Jiyao Guo
TAs: Andy Gray; Jake Easterling; Ralph F. Leyva Instructors: Dr. A. Antonio Arroyo Dr. Eric M. Schwartz

## Slide 2: What does it do?
Tracking a human
Sometimes help people carry their lunch box
Self-parking in certain area
Send a warning and stand still when it loses the target

## Slide 3: How does it do it?
Human identification:
A big QR code on the back
And also color identification on a walking stick

## Slide 4: How does it do it?
Motion control:
a PID controller is used for robot giving order to motors according to the difference between position of object in the camera
the camera can be rotated with three fixed angles

## Slide 5: How does it do it?

## Slide 6: Self-parking
A LED will be lighted at the top of the walking stick
Robot gets the signal
A QR code will be set at the parking place
Robot looks around and tracks the parking QR code to the parking place

## Slide 7: Component
ITEM | NUM | DESCRIPTION | REASON TO CHOOSE
Microcontroller |  |  | 
Arduino Mega 2560 R3 | 1 | Input voltage – 7-12V 54 Digital I/O Pins (14 PWM outputs) 16 Analog Inputs 256k Flash Memory 16Mhz Clock Speed | High speed with plentiful pins.
High Level Development Boards |  |  | 
Odroid XU4 | 1 | Samsung Exynos5422 Cortex™-A15 2Ghz and Cortex™-A7 Octa core CPUs 2GB LPDDR3 RAM PoP stacked eMMC5.0 HS400 Flash Storage 2 x USB 3.0 Host, 1 x USB 2.0 Host | High processing speed for image.
Sensors |  |  | 
USB-Cam 720p | 1 | The main USB camera | Provide high quality video. Work great with Odroid XU4
Mihappy 3pcs Ultrasonic Module | 3 | Ultrasonic sensors | Used to sense the obstacle.

## Slide 8: Component
ITEM | NUM | DESCRIPTION | REASON TO CHOOSE
Robot Body |  |  | 
Cherokey 4WD Mobile Robot | 1 | Embedded the L298P motor driver chip which allows to drive two 6-12V DC motors with maximum 2A current. Aluminum alloy body. | Come with 4 motors with motor driver. However, encoder is not included.
WiFi Module 4 | 1 |  | Used for provide WIFI access to Odroid.
Cooling Fan | 1 |  | Used to cooling the board
Encode | 2 | With hall sensors or laser sensors | To get the speed feedback for motors
Servo | 1 | HS-311 Standard | Used to rotate the camera
Battery | 1 |  | A battery of output of 7.4V is needed to power the Arduino, Odroid, 4 motors and the servo.

## Slide 9
The End