# 5 DOF Arm

## Overview

The two arms discussed below are five degree-of-freedom (5DOF) serial link manipulators.  Constructed from aluminum and plastic, the arms were designed to perform similar to that of a human arm.  Upper and lower arm lengths are proportional to that of an adult human.  Explosion of kinematics equations were kept to a minimum by aligning the axis of rotation from joint to joint.  Once attached to Pneuman, the arms will function both as an experimental apparatus and as an entertainment.  As shown below in figure01, the arms are mirror images of each other and are identical in all other respects.

## Joint Configuration

When designing a higher nth order DOF serial link manipulator, one must consider the kinematics equations behind each joint placement.  The arm was designed so that joint axis i intersects joint axis i+1, where i is the number of joints in the arm.  Each new link is offset from the previous link by 90( as shown in figure 02.

Joints ShoulderA, ShoulderB, and ElbowA are coincident at the shoulder.  This alignment allows for the arm to rotate as if a ball and socket joint were implemented.  ElbowB and WristA joints are also coincident.  Joints ShoulderA, ShoulderB, and ElbowB are actuated by linear actuators.  The remaining joints, ElbowA and WristA, are actuated by rotary actuators.

FIGURE 02	Arm kinematics.  The arrows indicate direction of rotation.  The thick lines represent the links.

Table 01 describes the joint characteristics along with the motor used.

TABLE 01	Joint characteristics.

## Kinematics

### DH Parameters

## Actuators

After weighing the pros and cons of a number of actuator schemes, it was found that dc motors would provide the needed torque with the least complexity.  However, dc motors do present problems when implemented in robotic systems.  These complex systems rely on precision and repeatability.  DC motors produce backlash, which throws off precision and thereby repeatability.  To help remedy this problem a revolute series elastic actuator (SEA) has been devised; see figure07 under Force Feedback Mechanism.  The revolute SEA will reduce backlash and will provide force feedback at the joint.  The SEA also promotes robustness and compliance throughout the arm.  Figure 03 depicts a basic representation of a SEA.  A spring is placed inline with the transmission shaft to reduce unwanted backlash and problems that may arise due to a sudden impact of a link with an object.

FIGURE 03	Series elastic actuator (SEA).

Two brands of surplus motors were purchased; one having a stall torque of 320 oz in and the other 200 oz in.  Although these motors would suffice, gear reduction at specified joints was immanent.  Two joints that did not require any gear reduction other than that of the gearbox were ElbowA and WristA.  Directly driven, these two joints proved more than the required range of motion and max speed.  Table 02 describes the characteristics of the dc motors.

TABLE 02	DC motor characteristics.

### Linear Actuator

### Rotary Actuator

One of the problems encountered when designing the rotation aspects of the upper arm was to align the ShoulderB joint perpendicular with the ElbowB axis.  A pulley drive system was implemented to overcome this problem.  The advantage of a pulley drive system is its compactness compared to the linear actuator.  In a pulley drive system there is no need for a lever arm or a screw-jack.  Another advantage over the jackscrew is that it increases the available rpm at the joint it actuates.  The SEA’s axis of rotation is coincident with that of the joint’s axis.  Below in figure 05 the motor pulley is rigidly attached to the motor shaft.  The cable is wrapped around the motor pulley and partly around the joint pulley.  Both ends of the cable are terminated on the joint pulley.  One is static while the opposite end is attached to a cable-tensioning device.  The cable-tensioning device is necessary to keep the cable taut at all times.  An “intelligent” tensioning device such as an inline memory-shape alloy extension spring may be implemented in a later version of the rotary actuator.

FIGURE 05	Rotary actuator drive system.

## Sensors

### Joint angle position

## Force Feedback Mechanism

Robot manipulator arms are precise when it comes to movement, yet are poor at sensing applied force.  When a manipulator arm is exposed to an object either intentionally or unintentionally, it has no way of sensing the applied force unless equipped with a force sensor.  Force sensors are used to regulate arm motion, but may also be used to deal with contact forces.  In order to overcome this shortfall in our robot arms, force sensing resistors (FSR) have been imbedded within the rotary SEA to provide sufficient force feedback.

The static mechanics in figure 06 are as follows:

- The motor is rigidly attached to link A.

- ‘A’ is rigidly attached to the motor shaft.

- ‘B’ is rigidly attached to link B.

- Two FSR are rigidly attached to opposite sides of the inner wall of ‘B’.

- Both ends of the spring are rigidly attached the individual FSR surfaces.

Note that the motor shaft will not be attached directly to ‘A’.  A pulley system will interface between ‘A’ and the motor shaft thereby increasing output torque.

FIGURE 06	Series elastic actuator (SEA) with motor.

Now, a dynamic description of figure 07:

- Normal Operation:

  - When the motor rotates, ‘A’ and ‘B’ are coincident and will rotate together.

- “Joint Overload” Operation:

  - When the motor rotates, ‘A’ will rotate yet resisting force on link B will not allow ‘B’ to rotate.  Therefore, the spring will compress.

  - When the spring compresses, the FSR senses a change in force applied.  This change in applied force is linearly related to the change in rotation between ‘A’ and ‘B’.

FIGURE 07	Dynamic description of revolute SEA.

## Electronics

# Text boxes

WristA

ElbowB

ElbowA

ShoulderB

ShoulderA

Z5

X5

Y5

Z3

X3

Y3

X4

Y4

Z4

X2

Y2

Z2

Z1

X1

Y1

{5}

{4}

{3}

{2}

{1}