| Digikey Part No | Mfg Part No | Description | Qty Needed | MAVRIC Part Position | Photo |
| --- | --- | --- | --- | --- | --- |
| ATMEGA128-16AC-ND | ATMEGA128-16AC | IC AVR MCU 128K 16MHZ COM 64TQF | 1 | U1 | * |
| 296-13082-1-ND | MAX3222CDBR | IC DRVR/RCVR MULTCH RS232 20SSOP | 1 | IC6 | * |
| AT24C256W-10SI2.7-ND | AT24C256W-10SI-2.7 | IC SEEPROM 256K 2.7V WIDE SO-8 | 1 | IC3 | * |
| 428-1004-ND | CY7C1019B-15VC | IC SRAM 128KX8 ASYNC WIDE 32SOJ | 1 | IC1 | * |
| DS1307Z-ND | DS1307Z | IC RTC SERIAL 512K 8-SOIC | 1 | IC3 | * |
| 296-4756-1-ND | SN74AHCT573DBR | IC OCTAL TRANSP LATCH 20-SSOP | 1 | IC5 | * |
| 296-11108-1-ND | UA7805CKTER | IC VOLT REG POS 5V 1.5A 3-PFM | 1 | IC4 | * |
| 296-1112-1-ND | SN74AHCT1G04DBVR | IC SNGL INVERTER GATE SOT-23-5 | 1 | T2 | * |
| P10KGCT-ND | ERJ-3GEYJ103V | RES 10K OHM 1/10W 5% 0603 SMD | 6 | R1, R4, R5, R9, R10, R11 | * |
| P4.7KGCT-ND | ERJ-3GEYJ472V | RES 4.7K OHM 1/10W 5% 0603 SMD | 2 | R2, R3 | * |
| 311-470ACT-ND | 9C08052A4700JLHFT | RES 470 OHM 1/8W 5% 0805 SMD | 1 | R6 | * |
| 308-1154-1-ND | CDRH62B-100MC | POWER INDUCTOR 10UH 1.10A SMD | 2 | L1, L2 | * |
| PCC220ACVCT-ND | ECJ-1VC1H220J | CAP CERAMIC 22PF 50V 0603 SMD | 2 | C13, C14 | * |
| PCC1794CT-ND | ECJ-1VF1E104Z | CAP .1UF 25V CERAMIC Y5V 0603 | 14 | C1, C2, C3, C4, C5, C6, C7, C8, C9, C10, C11, C12, C15, C16 | * |
| PCC1926CT-ND | ECJ-3YB1E564K | CAP .56UF 25V CERAMIC X7R 1206 | 4 | C19, C20, C21, C22 | * |
| PCE3417CT-ND | EEV-FK1V470P | CAP 47UF 35V ELECT FK SMD | 2 | C17, C18 | * |
| XC488CT-ND | ECS-.327-12.5-17-TR | CRYSTAL 32.768KHZ 12.5PF SMD | 2 | Q2, Q3 | * |
| XC694CT-ND | ECS-160-20-5P-TR | CRYSTAL 16.00MHZ 20PF SMD | 1 | Q1 | * |
| XC692CT-ND (Optional 14.7456 MHz instead of 16 MHz) | ECS-147.4-20-5P-TR | CRYSTAL 14.7456MHZ 20PF SMD | 1 | Q1 | * |
| 160-1166-1-ND | LTST-C150AKT | LED AMBER CLEAR 1206 SMD | 1 | LED1 | * |
| DL4004DICT-ND | DL4004-13 | RECTIFIER GPP 400V 1A SMD MELF | 1 | D1 | * |
| LL4148DICT-ND | LL4148-13 | DIODE SWITCH 75V 500MW MINIMELF | 1 | D2 | * |
| CT21912MST-ND | 219-12MST | SWITCH TAPE SEAL 12 POS SMD | 1 | DIP1 | * |
| 3000K-ND | 3000 | HOLDER BATTERY COIN 12MM DIA SMD | 1 | RTC STBY | * |
| The following item is .1 inch screw terminals that can optionally be used for the port headers. |
| 277-1279-ND | 1725711 | CONN TERM BLOCK 2.54MM 8POS | 8 | JP1, JP2, JP3, JP4, JP5, JP6, JP7, JP8 | * |

Headers

- .1 inch dual row headers: 2 2x5 (JP12, JP13)

- .1 inch single row headers: 2 1x3 (UART 0, UART 1) and 8 1x8 (JP1, JP2, JP3, JP4, JP5, JP6, JP7, and JP8)