STEVE

(Speed Trap Enforcement VehiclE)

Michael Hattermann

Final Report

EEL 5666 – Intelligent Machines Design Lab

Spring 2001

April 23, 2001

Table of Contents

Table of Contents	2

Abstract	3

Introduction	5

Integrated System	5

Mobile Platform	7

Actuation	8

Sensors	11

Sharp GP2D12 Analog IR Sensors	11

Bump Switches	12

Speed Trap Sensor	13

Hacked LiteOn Analog IR Sensors	19

Behaviors	21

Object Avoidance	21

Object Following	22

Conclusion	24

Documentation	25

Appendix A - Part Information	26

Appendix B – Source Code	27

Abstract

The purpose of this project is to construct an intelligent mobile robot to enforce a speed trap.  This Speed Trap Enforcement VehiclE (STEVE) will sit in place and wait for an object to pass.  When an object goes by, STEVE will calculate the speed the object was traveling.  If the object was exceeding a predetermined speed limit, STEVE will turn on his lights and siren and will begin to follow the speeding object.  If STEVE ever loses sight of the speeder, the siren will turn off and STEVE will perform object avoidance.  STEVE will attempt to “pull over” the speeding object by bumping it from behind.  Finally, if STEVE is able to pull the object over, he will signal success and then will shutdown, turning off his lights and siren, and will wait to be placed back in the speed trap.

Executive Summary

STEVE is an autonomous speed trap enforcement vehicle.  He is designed to work in a very simple, specially designed speed trap.  He must be placed in the speed trap to begin.  STEVE will wait there until a speeder is detected using two laser break-beam sensors.  Then STEVE will turn on his lights and siren and attempt to follow the speeding object.  If STEVE ever loses the speeder, he will turn off his siren and avoid obstacles until he finds the speeder again.  STEVE will then pull over the speeding object by bumping it.

STEVE’s brain, which is a Motorola HC12 mounted and a board custom designed for EEL4744, is powered by eight 1.2V Ni-Cd batteries.  Two output ports and 24k of SRAM have been added to the board.  STEVE moves along using two DC gear head motors, which are powered by 12 1.2V Ni-Cd batteries, and a castor wheel for balance.  The power supply and the control lines for the motors are completely isolated from the power supply of the electronics.  All of this is mounted in a custom platform made of balsa wood and designed and painted to look like a real police car.

STEVE uses a specially designed speed trap sensor, consisting of two laser pointers, two phototransistors, two IR LED’s, and two IR detectors modulated at 56.5kHz, to determine the speed of a passing object.  STEVE uses three Sharp GP2D12 analog IR rangefinders, modulated at 40kHz, and 7 bump switches to avoid obstacles.  STEVE also uses three hacked LiteOn analog IR detectors to follow an object.  STEVE is equipped with red and blue flashing lights and a siren for feedback.

Introduction

Do you ever think cops are wasting time and money by just sitting on the side of the road waiting to catch speeders?  Don’t you think they should be off trying to catch bad guys?  Well, now they can.  STEVE was designed to pull over speeders autonomously and automatically.  He won’t be sympathetic to girls crying or sob stories from drivers who just don’t  want a ticket.  STEVE can be much more efficient than your typical cop.  Now real cops can do more important things like catching murders and drug dealers.

Integrated System

STEVE’s brain is a Motorola HC12 microprocessor, running at 4Mhz, which is surface mounted on a custom board designed by Scott Kanowitz and Patrick O’Malley for EEL4744.  The HC12 has four pulse width modulation (PWM) channels, eight analog-to-digital (A/D) channels and eight input capture/output compare channels.  The board contains an Altera CPLD, which is used for memory expansion, 8k of EEPROM with a custom monitor program (used for downloading and debugging code) and an RS232 serial interface that connects to a computer through a 9-pin serial cable.  The board also contains a large prototyping area (roughly 3” x 8”).  A picture of the board can be seen in Figure 1.

A memory expansion was built in the prototyping area consisting of 24k of memory mapped SRAM (although only about 8k of it is usable due to unexplained technical difficulties).  There are also two 8-bit output ports.  The first one is constructed using two Fairchild DM9368 chips connected to a dual 7-segment display and is used to display the speed of objects passing through the speed trap.  The other is consists of a 74HC574 setup to drive 8 LED’s (which will be the flashing lights on top of the car).

Figure 1

There is a low battery indicator circuit built onto the board that will light up when the battery voltage drops below 7.8V.  The circuit schematics can be found in Figure 2.

Figure 2

Finally, there are four 4N25 optoisolators used to optically isolate the motors from the electronics.  There is a direction and a PWM signal for both the left and right motors.  All four optoisolators are wiring in exactly the same way, except for the input signal.  The schematic for one optoisolator is found in Figure 3.

Figure 3

STEVE utilizes an off-board speed tracking system (which will be discussed in detail later) to calculate the speed of a passing objects.  He uses two LiteOn digital IR receivers modulated at 56.5 kHz to communicate with the off-board speed tracking system. He uses 7 bump switches and 3 Sharp GP2D12 analog range finders to perform object avoidance.  Finally he uses 3 analog hacked LiteOn IR receivers modulated at 56.5 kHz to follow the speeding object.

Mobile Platform

The mobile platform for the robot was custom built out of 1/8 inch thick balsa wood.  The platform was designed using AutoCAD and cut out using a T-Tech machine in lab.  There were two primary design goals for the platform: 1) The platform had to be large enough to mount the electronics board and all of the sensors and 2) The platform had to look similar to a police car.

The electronics board is fairly large (6” x 8”).  This is the main reason the platform is fairly large.  The wheels were placed toward the back of the robot to make it look more like a car.  There is also a second layer to the platform, like the roof of a car, where the lights and siren are mounted.  This second layer also helps to hide the wires and electronics.  Finally, the platform was painted to resemble a University of Florida Police Department (UPD) car.  A picture of the completed platform can be found in Figure 4.

Figure 4

Actuation

STEVE needs to move fairly quickly if he is to catch speeding robots.  To get the desired speed, STEVE moves using two DC gear-head motors.  They have a no load speed of about 70 rpm and can deliver around 78 oz-in of torque.  They each draw about 220mA of current with no load and about 1.1 amps stall current.  The motors are driven by two National Semiconductor LMD18200T H-bridges located on a motor driver board originally designed for the OO-PIC, but still works for this application.  The schematic for the relevant parts of the board can be found in Figure 5.

Figure 5

The H-bridges can deliver up to 3 amps of continuous current and 6 amps peak current.  There are also two 3-amp fuses located on the board to ensure that the chips are not blown.  Each chip uses three control signals to control the motor: a) a PWM signal to control speed b) a direction signal to indicate forward or backward and c) a brake signal.  The brake has been hard wired to be off for both motors.

Figure 6

The motors and the motor driving board are both mounted on the bottom of the platform.  Figure 6 contains a picture of both.  A 3-inch wheel is attached to each motor.  This was done by first super gluing roll pins into the center axis of each wheel and then using JB Weld to cold weld the roll pins to the motors. There is a castor wheel attached to the front of the platform to balance the robot and allow free movement.

The motor control software is fairly complicated.  The motor speed and direction values are updated every 65ms by an RTI interrupt using the following formula:

The value chosen for was 6.  Then whenever a behavior wants to change the motor speeds, it just has to write to the DesiredSpeed (called NLEFTSPD and NRIGHTSPD in the code, for the left and right motors respectively) global variable, and the motors will be updated automatically.

There is also a function that provides the behaviors with basic control maneuvers.  The maneuvers provided are: 1) go forward, 2) go backward, 3) hard left, 4) hard right, 5) soft left,  6) soft right, 7) stop, 8) backup left and 9) backup right.  This function will set the motors to perform these maneuvers at whatever the current maximum speed is.

Sensors

Sharp GP2D12 Analog IR Sensors

Three Sharp GP2D12 analog range-finding sensors are used to perform obstacle avoidance.  These sensors continuously emit a very narrow beam of IR, modulated at 40kHz.  They also continuously check for the amount of IR returned to the sensor using an IR detector.  By the amount of IR returned, you can get a fairly accurate reading as to how far away something is.  This distance is returned as an analog value.

A test was conducted to find the values returned for an object being a certain distance away.  The sensor was set in a stationary position, and an object was moved farther and farther away, taking readings along the way.  Also, the width of the beam at each position was measured.  Table 1 contains the data from the test.

| Distance | Reading 1 | Reading 2 | Reading 3 | Width of beam |
| --- | --- | --- | --- | --- |
| 4mm | 38 | 35 | 37 | - |
| 8mm | 55 | 55 | 54 | - |
| 12mm | 6B | 6C | 6B | - |
| 16mm | 87 | 87 | 86 | .55mm |
| 20mm | 78 | 7A | 79 | .6mm |
| 24mm | 66 | 66 | 66 | .6mm |
| 28mm | 59 | 59 | 59 | .6mm |
| 32mm | 4F | 4F | 50 | .6mm |
| 36mm | 47 | 46 | 47 | .6mm |
| 40mm | 40 | 40 | 40 | .6mm |
| 44mm | 3B | 3C | 3B | .6mm |

Table 1

The test shows that the measurements obtained from the sensor are very linear when the object 16mm (about 3 inches) away or farther.  Also, it is important to notice that the width of the beam is narrow (about 1/4 inch).

Bump Switches

Seven bump switches are used to detect if STEVE has collided with an object.  These switches have two purposes: 1) redundancy in obstacle avoidance and 2) to tell when a speeding object has been pulled over.  If the GP2D12 analog IR sensors fail to find an obstacle, the bump switches will tell STEVE that he has hit something.  Then STEVE can take the proper corrective action.  Also, STEVE pulls over a speeding object by bumping it from behind.  The bump switches will also let STEVE know when this has been accomplished.

Figure 7

Figure 7 contains the circuit diagram of the bump sensor network.  All of the bump switches are wired together through a resistor network and are connected to an analog port on the HC12.  When a bump switch (or any combination of bump switches) is pressed, a unique value will be read from the analog port.  A test was conducted to determine the values for each combination of switches.  Table 2 contains the data from that test.

| Bumper(s) | Resistance | Test1 | Test2 | Test3 | Test4 | Test5 |
| --- | --- | --- | --- | --- | --- | --- |
| LF | 4.7k | AE | AE | AF | AE | AF |
| CF | 10k | 82 | 82 | 82 | 82 | 82 |
| RF | 22k | 50 | 50 | 50 | 50 | 50 |
| LF+CF | 3.2k | C3 | C3 | C3 | C3 | C4 |
| RF+CF | 6.9k | 99 | 99 | 9A | 9A | 9A |
| LF+RF | 3.9k | BA | BA | B9 | B9 | B9 |
| LF+CF+RF | 2.8k | CA | CA | CA | CA | CA |
| LR | 47k | 2C | 2C | 2C | 2C | 2C |
| CR | 100k | 17 | 17 | 17 | 17 | 17 |
| RR | 220k | 0B | 0B | 0B | 0B | 0B |
| LR+CR | 32k | 3C | 3C | 3D | 3C | 3C |
| RR+CR | 68.8k | 20 | 20 | 20 | 20 | 21 |
| LR+RR | 38.7k | 34 | 34 | 34 | 34 | 34 |
| LR+CR+RR | 27.9k | 43 | 43 | 43 | 43 | 43 |

Table 2

Speed Trap Sensor

STEVE determines the speed of passing objects using a special speed trap sensor.  This sensor operates much like a real speed trap.  In a real speed trap, there are two white lines painted on the road.  The police then fly a plane above the road and time cars as they go by.  They start the timer when the car crosses the first line and stop it when it crosses the second line.  Then, by knowing the distance between the lines and the time it took to travel that distance, the average velocity of the car is calculated.  If the car is speeding, the plane will radio down to police officers waiting farther down the road and they will pull over the car.

### Figure 8

STEVE’s speed trap operates in the same way.  Figure 8 contains an overhead diagram of the speed trap.  The white lines of the speed trap are created using two laser break beams.  When a beam is broken, the control circuitry will “radio” to STEVE using an IR emitter modulated at 56.5kHz that the beam is broken.  STEVE then records the time the beam was broken.  Once both beams are broken, STEVE calculates the time it took the object to travel from one beam to the other.  Then, knowing the beams are two feet apart, STEVE calculates the average velocity of the moving object and determines if it was exceeding some predetermined speed limit.  If the object is speeding, STEVE turns on his lights and siren and tries to pull it over.  If the object is not speeding, STEVE lets it go and continues to wait for a speeding object.

The control circuitry for the break beam sensor is very simple.  It consists of three parts: a timer to generate a 56.5kHz waveform and two control circuits to monitor the break beam.  The circuit diagram of the timer can be found in Figure 9.

### Figure 9

A 555 timer chip was used to generate the 56.5kHz signal needed to modulate the IR emitter.  The timer is running in the astable mode of operation and has a duty cycle of 48.4%.  The potentiometer can be used to change the frequency from 56.7kHz down to 29.9kHz.  This allows IR detectors at different frequencies to be used if there are interference problems.

There are two identical control circuits to control the break beam sensors.  The circuit diagram for one control circuit can be found in Figure 10.  The LM358 op amp is used to convert the signal from the phototransistor to a digital signal.  This is signal is then passed through a 74’02 which AND’s it with the 56.5kHz signal generated from the timer circuit.  This will generate a 56.5kHz signal at the output of the 74’02 whenever the beam is broken.

### Figure 10

This signal is then fed through the IR emitter to “radio” to STEVE that the beam has been broken.  There is also a feedback LED to indicate when the beam is connected to help in the setup of the speed trap.

An experiment was designed to find the maximum distance between the laser pointer and the phototransistor.  A photo transistor was set in place and a laser pointer was set up in front of it.  Then the laser pointer was moved back gradually, recording the distance the status of the beam at each step.  The results of this experiment can be found in Table 3.

| Distance(feet) | Test 1 | Test 2 | Test 3 |
| --- | --- | --- | --- |
| ½ | Yes | Yes | Yes |
| 1 | Yes | Yes | Yes |
| 2 | Yes | Yes | Yes |
| 3 | Yes | Yes | Yes |
| 4 | Yes | Yes | Yes |
| 5 | Yes | Yes | Yes |
| 6 | Yes | Yes | Yes |

### Table 3

The results of the experiment show that the laser can be placed very far from the phototransistor and the break beam will still work.  This experiment was limited by the length of wire I had to connect to the laser pointer.  Also, the farther away from the phototransistor the laser pointer was moved, the more difficult it was to keep the laser pointer aimed at the phototransistor.  This was mainly due to the poor design of the laser pointer holders.  However, for the intended use of the sensor, three feet of separation is more than sufficient.

An experiment was designed to see how the break beam sensor worked under different lighting conditions.  It is difficult to measure the actual amount of light in a room, so a rough scale was made ranging from dark to bright.  Then, as the amount of light in the room was changed, the connectedness of the beam was recorded.  Table 4 contains the results from the experiment.

| Brightness | Test 1 | Test 2 | Test 3 |
| --- | --- | --- | --- |
| Dark | Yes | Yes | Yes |
| Below Average | Yes | Yes | Yes |
| Average | Yes | Yes | Yes |
| Above Average | Yes | Yes | Yes |
| Bright | Yes | Yes | Yes |
| Very Bright | No | No | No |

### Table 4

Under the most extreme lighting conditions (i.e. a 60 Watt light bulb being shined from 1-2 feet away), the break beam sensor failed.  Under all other conditions, the beam was working.  These results are acceptable, because the break beam is very insensitive to ambient light.  This is more than sufficient because STEVE will always run indoors.

An experiment was designed to test the maximum distance the IR emitter can communicate with STEVE.  A break beam sensor and IR emitter were set in place, and STEVE was move progressively farther away.  At each step, the break beam was broken and STEVE was checked to see if he received the communication.  Table 3 contains the data from the experiment.

| Distance(inches) | Test 1 | Test 2 | Test 3 |
| --- | --- | --- | --- |
| 2 | Yes | Yes | Yes |
| 4 | Yes | Yes | Yes |
| 6 | Yes | Yes | Yes |
| 8 | Yes | Yes | Yes |
| 10 | Yes | Yes | No |
| 12 | No | No | No |
| 14 | No | No | No |

### Table 5

The results of the experiment show that STEVE can be up to 8 inches away from the IR emitter and safely receive the broken beam signal.  Any farther away from that, and he is not guaranteed to accurately receive the signal.  For the intended use of the sensor, 8 inches is more than enough distance to safely communicate with STEVE.

Hacked LiteOn Analog IR Sensors

Three analog IR sensors are needed to perform object following.  These sensors also had to be at a different frequency than the obstacle avoidance IR sensors.  The only Sharp cans I found were at 38kHz or 40kHz, which would interfere with the obstacle avoidance sensors.  So I purchased several LiteOn digital IR receivers modulated for 56.5kHz and set out to hack them to be analog.  After several hours and a lot of probing, I found the hack.  It is pictured in Figure 11.

Figure 11

The first step is to open the can to get access to the electronics inside.  When the can is open, the electronics board inside should look like Figure 11A.  There is on main black chip with eight pins, several surface mount resistors, the bottom of solders for components on the other side of the board, and traces connecting them.  The next step is to cut the two traces that connect to the output pin.  This is shown in Figure 11B.  The final step is to solder a jumper (i.e. a piece of wire wrap wire) between the output pin and the bottom of a solder, as shown in Figure 11C.

An experiment was designed to test the range of the hacked LiteOn IR receiver.  The receiver has held stationary and an IR LED was moved incrementally farther away.  Several readings were taken from the sensor a each step along the way.  The results of the test can be found in Table 4.  It was found that the voltage on the out put pin varied from 1.575V when there was no IR to 2.530V  when the IR LED was less than one inch from receiver.

| Distance | Test 1 | Test 2 | Test 3 | Test 4 | Test 5 |
| --- | --- | --- | --- | --- | --- |
| 2” | 7F | 7F | 7F | 7F | 7F |
| 4” | 7F | 80 | 80 | 7F | 80 |
| 6” | 7D | 7D | 7D | 7D | 7D |
| 8” | 76 | 76 | 76 | 76 | 76 |
| 10” | 73 | 73 | 73 | 73 | 73 |
| 12” | 6F | 6F | 6E | 6F | 6F |
| 14” | 6A | 6A | 6A | 6A | 6A |
| 16” | 67 | 67 | 67 | 67 | 67 |
| 18” | 63 | 63 | 63 | 63 | 63 |
| 20” | 5F | 5F | 5F | 5F | 5E |
| 22” | 5C | 5C | 5C | 5C | 5C |
| 24” | 5A | 5A | 5A | 5A | 5A |
| 26” | 57 | 57 | 57 | 57 | 57 |
| 28” | 55 | 55 | 55 | 55 | 55 |
| 30” | 54 | 54 | 54 | 54 | 54 |
| 32” | 53 | 53 | 53 | 53 | 53 |
| 34” | 53 | 53 | 53 | 53 | 53 |
| 36” | 52 | 52 | 53 | 52 | 53 |
| 38” | 52 | 52 | 52 | 52 | 52 |
| 40” | 52 | 52 | 52 | 52 | 52 |
| Nothing | 50 | 50 | 50 | 50 | 50 |

Table 6

Behaviors

Object Avoidance

STEVE is able to move around while avoiding obstacles.  He does this using the three Sharp GP2D12 analog IR sensors and the 7 bump switches.  Figure 12 shows a diagram of where the sensors are located on the robot.

Figure 12

The three IR sensors form a grid and tell STEVE how far away on object is.  Then, depending on how far away the object is, STEVE will react using the preset maneuvers.  Figure 13 shows an approximate view of STEVE reactions to an object at varying distances.  Once a reaction is determined, then the decision to react left of right needs to be made.  To do this, STEVE looks at the values of the left and right IR sensors.  If one value is greater than the other by 16, then STEVE will turn away from that sensor.  Otherwise, if the left and right sensors are about equal, STEVE will turn in a random direction.  Once a random direction is chosen, STEVE will continue to turn that way until he changes reactions (i.e. changing from react soft to react hard).  Every time a new reaction starts, a new random direction is chosen.

Figure 13

Object Following

STEVE is able to follow a moving object, provided the object is emitting IR modulated at 56.5kHz.  STEVE uses three hacked LiteOn analog IR sensors to do this. The sensors are aligned so that they overlap to create five zones.  Each zone is then assigned a reaction value.  The alignment of the sensors and the associated reactions can be seen in Figure 14.  This makes the logic for following very simple.  If STEVE is ever in doubt as to which zone the object is in, he will react the same way he did last time (it is assumed the object wont move very far in the time between measurements).  Also, if the front bumper is pressed during following, the analog IR sensors for obstacle avoidance are checked.  If they indicate that an object is close, we assume that we ran into the speeding object.  At this point we terminate the program and wait to be placed back in the speed trap.

Figure 14

Conclusion

STEVE was the result of a lot of hard work.  He was built from scratch.  I assembled the entire electronics board.  I built the memory expansion.  The platform was designed, built and painted.  I found a new hack for a digital IR receiver.  I designed and built my unique speed trap sensor.  STEVE, in his current form, almost does everything he is supposed to do.  The only exception is the bumpers don’t work for obstacle avoidance.  The was a tremendous amount of noise on the bumper lines due to the electro-magnetic field generated by the motors.  A primitive Faraday cage was built using a Barq’s root beer can just to be able to use the front bumper of object following.  This problem can probably be fixed with a better Faraday cage, but I felt it was better to leave STEVE as he is: WORKING.

My biggest success is my DC motors.  The motors were a lot more work than servos, but they also perform much better.  A lot of research went into find the motor driving chips and board.  The motors also needed their own power source and to be optically isolated.  But the end result was very impressive from the smooth handling to the speed STEVE is able to obtain.

If I had to start this project over, I would definitely choose a different electronics board.  The board is nice, but I spent a ridiculous amount of time just trying to get the RAM memory expansion to work.  I might also purchase larger DC motors for more speed.  But other than that, I was very pleased with how STEVE ended up.

Documentation

Thanks to:

- Dr. Gugel and Scott Kanowitz for their help getting the memory expansion to work

- Rand Chandler for re-soldering my HC12 chip to my board

- Dr. Arroyo, Dr. Schwartz, and Aamir Qaiyumi for their help, guidance and abundance of new ideas to simplify and improve my robot

- National Semiconductor for the free motor driver chips I received

- Motor driver schematics from Magnevation (http://www.magnevation.com)

- Low battery circuit schematics from:

http://www.ee.washington.edu/conselec/Sp96/projects/jeddk2/final/ee498h.htm

- My parents and girlfriend for the support and encouragement throughout the semester

# Appendix A - Part Information

| Component | Vendor | Vendor Part# |
| --- | --- | --- |
| Laser pointers (Clearline Concepts) | Office Depot | 075235520052 Model CL2005 |
| IR Emitter/Detector Pair | Radio Shack | 276-142 |
| IR Detector Module (56.5kHz) | Jameco | 176541 |
| DC Gearhead Motors | Acroname | S5-GMOT-4 |
| 4N25 optoisolators | Jameco | 40985 |
| 32kx8 SRAM | Jameco | 75037 |
| Motor driver board (Magnevation) | Acroname | R105-DC-MOTOR-D |
| Piezo buzzer | Radio Shack | 273-065 |
| Batteries (Ni-Cd AA’s) | Radio Shack | 230-449 |
| Roll pins | Lowes | 138836 |
| Nylon spacers | Lowes | 136921 |
| 7-segment latch/driver chips (DM9368) | Digi-Key | DM9368N-ND |
| Motor driver chips (LMD18200T) | National Semiconductor | LMD18200T |

Appendix B – Source Code

* Filename      : SCI.ASM

* Programmer    : Michael Hattermann

* Date          : February 4, 2002

* Version       : 1.0

* Description   : This file contains SCI communication

*                  functions for input and output of

*                  data.  The following functions are

*                  available:

*

*                  WAIT_TC - wait for transmit complete

*                  SET_BAUD - change the baud rate

*                  TX_ON - turn transmitter on

*                  TX_OFF - turn transmitter off

*                  RX_ON - turn receiver on

*                  RX_OFF - turn receiver off

*                  RX_INT_ON - turn receiver interrupts on

*                  RX_INT_OFF - turn receiver interrupts off

*                  OUTCHAR - prints character to screen

*                  OUTSTR - prints string to screen

*                  INCHARWAIT - waits for character input

*                  INCHAR - get character input if any

*                  OUTNUM - prints number to screen

*                  NIBTOCHAR - prints nibble to screen

*                  OUTADDR - prints 16-bit num to screen

*                  INITSCI - turns on SCI for 9600 baud

*

*

*#define __DEBUGSCI_    1

#include "hc12.asm"

*

************************************************************

* SCI Equates

************************************************************

*

****Baud rate equates****

BAUD19200   EQU     0

BAUD14400   EQU     2

BAUD9600    EQU     4

BAUD4800    EQU     6

BAUD2400    EQU     8

BAUD1200    EQU     10

BAUD600     EQU     12

BAUD300     EQU     14

****ASCII character equates****

EOS         EQU     $04             ; User-defined End Of String (EOS) character

CR          EQU     $0D             ; Carriage Return Character

LF          EQU     $0A             ; Line Feed Character

ESC         EQU     $1B             ; ESC character

*

************************************************************

* SCI Test Program

************************************************************

*

#ifdef __DEBUGSCI_

ORG     $0900

HELLO       DC.B    'Hello world!!!'

NEWLINE     DC.B    CR,LF           ; Newline string

DC.B    EOS

PRESSKEY    DC.B    'Press any key to continue'

DC.B    CR,LF,EOS

CHANGETO    DC.B    'Change baud rate to: '

DC.B    EOS

PROMPT      DC.B    'Start typing...'

DC.B    CR,LF,EOS

TEST        LDAA    #$00            ; turn off COP watchdog timer

STAA    COPCTL

LDS     #$0bff          ; init the stack pointer

JSR     INITSCI         ; init SCI system

LDX     #HELLO          ; print "hello world"

JSR     OUTSTR          ;

LDX     #CHANGETO       ; print change baud message

JSR     OUTSTR          ;

LDX     #$1200          ; print new baud rate

JSR     OUTADDR         ;

LDX     #NEWLINE        ; print new line

JSR     OUTSTR          ;

LDX     #PRESSKEY       ; print "press any key"

JSR     OUTSTR          ;

JSR     INCHARWAIT      ; wait for character

LDAA    #BAUD1200       ; change baud rate

JSR     SET_BAUD        ;

LDX     #HELLO          ; print "hello world"

JSR     OUTSTR          ;

LDX     #$1234          ; test print address

JSR     OUTADDR         ;

LDX     #PROMPT         ; print prompt

JSR     OUTSTR          ;

HERE        JSR     INCHARWAIT      ; get character

JSR     OUTCHAR         ; echo to screen

BRA     HERE            ; end of program

#endif

*

************************************************************

* Constant Definitions

************************************************************

*

BAUDTBL     DC.W    13              ; (0) BAUD rate = 19200

DC.W    17              ; (1) BAUD rate = 14400

DC.W    26              ; (2) BAUD rate = 9600

DC.W    52              ; (3) BAUD rate = 4800

DC.W    104             ; (4) BAUD rate = 2400

DC.W    208             ; (5) BAUD rate = 1200

DC.W    417             ; (6) BAUD rate = 600

DC.W    833             ; (7) BAUD rate = 300

*

*******************************************************************************

*                       SUBROUTINE -  WAIT_TC

* Description: Waits for the current transmit operation to complete (polls the

*                TC flag in SCI status register 1)

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

WAIT_TC

BRCLR   SC0SR1,BIT6,WAIT_TC     ; wait until done sending

RTS                             ; Return to caller

*

*

*******************************************************************************

*                       SUBROUTINE -  SET_BAUD

* Description: Sets the baud rate to the rate specified in register A.  Reg A

*               can only take on these predefined values:

*       BAUD19200     = BAUD rate 19200

*       BAUD14400     = BAUD rate 14400

*       BAUD9600      = BAUD rate 9600

*       BAUD4800      = BAUD rate 4800

*       BAUD2400      = BAUD rate 2400

*       BAUD1200      = BAUD rate 1200

*       BAUD600       = BAUD rate 600

*       BAUD300       = BAUD rate 300

*

* Input         : New baud rate in reg A

* Output        : None.

* Destroys      : SC0BDH, SC0BDL.

* Calls         : None.

*******************************************************************************

*

SET_BAUD

PSHX                    ; Preserve reg X

LDX     #BAUDTBL        ; Load address of baud table

LDX     A,X             ; Load baud rate from table

STX     SC0BD           ; Set baud rate in register

PULX                    ; Restore reg X

RTS                     ; Return to caller

*

*******************************************************************************

*                       SUBROUTINE -  TX_ON, TX_OFF

* Description: Enables transmitter, disables transmitter

* Input         : None.

* Output        : None.

* Destroys      : SC0CR2.

* Calls         : None.

*******************************************************************************

*

TX_ON

BSET    SC0CR2,BIT3     ; turn on the transmitter

RTS                     ; return to caller

TX_OFF

BCLR    SC0CR2,BIT3     ; turn off the transmitter

RTS                     ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  RX_ON, RX_OFF,RX_INT_ON,RX_INT_OFF

* Description: Enables receiver, disables receiver, enables receive interrupts,

*               disables receive interrupts

* Input         : None.

* Output        : None.

* Destroys      : SC0CR2.

* Calls         : None.

*******************************************************************************

*

RX_ON

BSET    SC0CR2,BIT2     ; turn on the receiver

RTS                     ; return to caller

RX_OFF

BCLR    SC0CR2,BIT2     ; turn off the receiver

RTS                     ; return to caller

RX_INT_ON

BSET    SC0CR2,BIT5     ; enable receiver interrupts

RTS                     ; return to caller

RX_INT_OFF

BCLR    SC0CR2,BIT5     ; disable receiver interrupts

RTS                     ; return to caller

*

************************************************************************

*                       SUBROUTINE -  OUTCHAR

* Description: Outputs the character in register A to the screen

* Input         : Data to be transmitted in register A.

* Output        : Transmits the data.

* Destroys      : None.

* Calls         : WAIT_TC

************************************************************************

*

OUTCHAR

JSR     WAIT_TC         ; wait until transmitter is idle

STAA    SC0DRL          ; output character

RTS                     ; Return from subtoutine

*

************************************************************************

*                       SUBROUTINE -  OUTSTR

* Description: Outputs the string pointed to by X.  String must be

*               terminated by EOS character.

* Input         : String to be output in reg X

* Output        : Transmits the string.

* Destroys      : None.

* Calls         : OUTCHAR

************************************************************************

*

OUTSTR

PSHA                    ; preserve reg A

PSHX                    ; preserve reg X

OUTSTR1

LDAA    1,X+            ; Get a character (put in reg A)

CMPA    #EOS            ; Check if it's EOS

BEQ     OUTSTR2         ; Branch to Done if it's EOS

JSR     OUTCHAR         ; Print the character

BRA     OUTSTR1

OUTSTR2

PULX                    ; restore reg X

PULA                    ; restore reg A

RTS                     ; Return from subtoutine

*

************************************************************************

*                SUBROUTINE  -  INCHARWAIT

* Description: Waits for a character to be pressed and reads it into

*               reg A

* Input         : None

* Output        : Character pressed in reg. A

* Destroys      : A.

* Calls         : None

************************************************************************

*

INCHARWAIT

BRCLR   SC0SR1,BIT5,INCHARWAIT  ; wait until buffer full

LDAA    SC0DRL                  ; input character

RTS                             ; Return from subroutine

*

************************************************************************

*                SUBROUTINE  -  INCHAR

* Description: Checks to see if character recevied - if so returns the

*               character, if not returns 0

* Input         : None

* Output        : Character pressed in reg A; 0 if none

* Destroys      : A.

* Calls         : None

************************************************************************

*

INCHAR

BRCLR   SC0SR1,BIT5,INCHAR1     ; if there is no data, get out

LDAA    SC0DRL                  ; yes, read data

INCHAR1

RTS                             ; return to caller

*

************************************************************************

*                       SUBROUTINE -  OUTNUM

* Description: Outputs the number in register A to the screen

* Input         : Data to be transmitted in register A.

* Output        : Transmits the data.

* Destroys      : None.

* Calls         : NIBTOCHAR

************************************************************************

*

OUTNUM

PSHA                    ; preserve reg A

PSHA                    ; preserve reg A

ANDA    #%11110000      ; get upper nibble

LSRA                    ; shift it right to get the nibble

LSRA

LSRA

LSRA

JSR     NIBTOCHAR       ; change A and print it

PULA                    ; restore reg A

ANDA    #%00001111      ; get lower nibble

JSR     NIBTOCHAR       ; change A and print it

PULA                    ; restore reg A

RTS                     ; return to caller

*

************************************************************************

*                       SUBROUTINE -  NIBTOCHAR

* Description: Converts lower nibble of A to ASCII and prints it

* Input         : Data to convert in A.

* Output        : Transmits the data.

* Destroys      : None.

* Calls         : OUTCHAR

************************************************************************

*

NIBTOCHAR

CMPA    #9             ; is it greater than 9?

BGT     NIBTOCHAR1     ; if so, print a character

ADDA    #48            ; if not, print a number starting at 48 ASCII

BRA     NIBTOCHAR2     ;

NIBTOCHAR1

ADDA    #55            ; if so, print a letter starting at 55 = 65-10

NIBTOCHAR2

JSR     OUTCHAR        ; print it

RTS

*

************************************************************************

*                       SUBROUTINE -  OUTADDR

* Description: Outputs the number in reg X to the screen

* Input         : Data to print in X.

* Output        : Transmits the data.

* Destroys      : None.

* Calls         : OUTNUM

************************************************************************

*

OUTADDR

PSHD                    ; save reg D

TFR     X,D             ; load X into D

JSR     OUTNUM          ; prints whats in A -- MSB

TBA                     ; B -> A

JSR     OUTNUM          ; prints whats in B -- LSB

PULD                    ; restore D

RTS                     ; return to caller

*

************************************************************************

*                       SUBROUTINE - INITSCI

* Description: This subroutine initializes the BAUD rate to 9600 and

*              sets up the SCI port for 1 start bit, 8 data bits and

*              1 stop bit.  It also enables the transmitter and receiver

* Input         : None.

* Output        : Initializes SCI.

* Destroys      : None.

* Calls         : SET_BAUD,TX_ON,RX_ON

************************************************************************

*

INITSCI     PSHA                    ; save reg A

LDAA    #BAUD9600       ; set the baud rate to 9600

JSR     SET_BAUD        ;

JSR     TX_ON           ; turn on the transmitter

JSR     RX_ON           ; turn on the receiver

PULA                    ; restore reg A

RTS                     ; Return from subtoutine

*

************************************************************************

* Filename      : ATD.ASM

* Programmer    : Michael Hattermann

* Date          : February 22, 2002

* Version       : 1.0

* Description   : This file contains the Analog to

*                  Digital (A/D) conversion functions

*                  for the input of analog signals. The

*                  following functions are available:

*

*                   INITATD - Initializes the ATD system

*                   KILLATD - Shuts down the ATD system

*                   ANALOG - Returns ATD value for port specified

*

*#define __DEBUGATD_     1

#include "hc12.asm"

*

************************************************************

* A/D Equates

************************************************************

*

CHANNEL0    EQU     $00

CHANNEL1    EQU     $01

CHANNEL2    EQU     $02

CHANNEL3    EQU     $03

CHANNEL4    EQU     $04

CHANNEL5    EQU     $05

CHANNEL6    EQU     $06

CHANNEL7    EQU     $07

*

************************************************************

* A/D Channel Assignments

************************************************************

*

LEFTIR          EQU     CHANNEL0

RIGHTIR         EQU     CHANNEL1

CENTERIR        EQU     CHANNEL2

CENTERFOLLOW    EQU     CHANNEL4

LEFTFOLLOW      EQU     CHANNEL5

RIGHTFOLLOW     EQU     CHANNEL6

BUMPER          EQU     CHANNEL7

*

************************************************************

* A/D Debug Code

************************************************************

*

#ifdef __DEBUGATD_

ORG     USERPROG_PVECT

JMP     TEST

ORG     $B000

TEST        LDAA    #$00            ; turn off COP watchdog timer

STAA    COPCTL

LDS     #$0bff          ; init the stack pointer

JSR     INITATD         ; init A/D system

JSR     INITSCI         ; init SCI system

MOVB    #$80,TSCR       ; enable the timer

HERE

*            LDX     #LEFT           ; print left IR message

*            JSR     OUTSTR          ;

LDAA    #CHANNEL7       ; get left IR value

JSR     ANALOG          ;

JSR     OUTNUM          ; print value

LDX     #NEWLINE        ; print newline

JSR     OUTSTR          ;

*            LDX     #RIGHT          ; print right IR message

*            JSR     OUTSTR          ;

*            LDAA    #CHANNEL1       ; get right IR value

*            JSR     ANALOG          ;

*            JSR     OUTNUM          ; print value

*            LDX     #NEWLINE        ; print newline

*            JSR     OUTSTR          ;

LDX     #500            ; wait 1/2 second

JSR     WAIT            ;

BRA     HERE            ; end of program

LEFT        DC.B    'Left IR value = '

DC.B    EOS

RIGHT       DC.B    'Right IR value = '

DC.B    EOS

NEWLINE     DC.B    CR,LF           ; Newline string

DC.B    EOS

#include "sci.asm"

#include "wait.asm"

#endif

*

*******************************************************************************

*                       SUBROUTINE -  INITATD

* Description: Initializes the analog to digital converter

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

INITATD     PSHA                        ; save reg A

MOVB    #$80,ATDCTL2        ; turn on ATD system

MOVB    #$00,ATDCTL3        ; enable conversions in bgnd mode

MOVB    #$01,ATDCTL4        ; setup conversion rate = 2MHz

LDAA    #195                ; load loop counter

INITATD1    NOP                         ; wait for ATD to power up

DBNE    A,INITATD1          ; if we still need to wait, wait

PULA                        ; restore reg A

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  KILLATD

* Description: Shuts down the analog to digital converter

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

KILLATD     MOVB    #$00,ATDCTL0        ; stop current conversion (if there is one)

MOVB    #$00,ATDCTL2        ; turn off ATD system

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  ANALOG

* Description: Converts the analog channel specified by reg A and returns the

*               converted value in reg A.  Valid values for channel are (the

*               equates an be found above):

*

*                   CHANNEL0    - A/D Channel #0

*                   CHANNEL1    - A/D Channel #1

*                   CHANNEL2    - A/D Channel #2

*                   CHANNEL3    - A/D Channel #3

*                   CHANNEL4    - A/D Channel #4

*                   CHANNEL5    - A/D Channel #5

*                   CHANNEL6    - A/D Channel #6

*                   CHANNEL7    - A/D Channel #7

*

* Input         : Channel to convert in reg A.

* Output        : Digital value of channel in reg A.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

ANALOG      STAA    ATDCTL5                     ; start conversion on channel specified

ANALOG1     BRCLR   ATDSTATH,BIT7,ANALOG1       ; wait for conversion to complete

LDAA    ADR2H                       ; load conversion result

RTS                                 ; return to caller

*

************************************************************************

* Filename      : PWM.ASM

* Programmer    : Michael Hattermann

* Date          : February 22, 2002

* Version       : 1.0

* Description   : This file contains the pulse width

*                   modulation functions for generating

*                   an output waveform.  The following

*                   functions are available

*

*                       INITPWM - inits PWM system

*                       KILLPWM - shut down PWM system

*                       LEFTMOTOR - sets spd,dir for left motor

*                       RIGHTMOTOR - sets spd,dir for right motor

*                       CHNGSPEED - sets new speed for motors

*                       STEER - sets motors to perform known manuevers

*                       PULLOUT - move to begin chase

*

*

*#define __DEBUGPWM_     1

#include "hc12.asm"

*

************************************************************

* PWM Equates

************************************************************

*

PWM0        EQU     0           ; left motor

PWM1        EQU     1           ; right motor

PWM2        EQU     2

PWM3        EQU     3

PWM4        EQU     4           ; left direction

PWM5        EQU     5           ; left brake

PWM6        EQU     6           ; right direction

PWM7        EQU     7           ; right brake

ACCELCONST  EQU     6           ; acceleration constant

FULLSPEED   EQU     200

_7_8_SPEED  EQU     175

_3_4_SPEED  EQU     150

_5_8_SPEED  EQU     125

HALFSPEED   EQU     100

_3_8_SPEED  EQU     75

_1_4_SPEED  EQU     50

_1_8_SPEED  EQU     25

STOPSPEED   EQU     0

LEFTDIR     EQU     BIT6

LEFTBRK     EQU     BIT7

RIGHTDIR    EQU     BIT4

RIGHTBRK    EQU     BIT5

GOFOWARD    EQU     0

GOBACK      EQU     1

HARDLEFT    EQU     2

SOFTLEFT    EQU     3

HARDRIGHT   EQU     4

SOFTRIGHT   EQU     5

BACKLEFT    EQU     6

BACKRIGHT   EQU     7

STOP        EQU     8

*

************************************************************

* PWM Debug Code

************************************************************

*

#ifdef __DEBUGPWM_

ORG     USERPROG_PVECT

JMP     TEST

ORG     $B000

TEST

JSR     INITPWM         ; initialize the PWM system

LDD     #HALFSPEED      ; load speed

JSR     CHNGSPEED       ; set max speed of motors

TEST1

LDX     #GOFOWARD       ; load manuever

MOVB    #GOFOWARD,SEG7PORT      ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 1 sec

JSR     WAIT            ;

LDX     #GOBACK         ; load manuever

MOVB    #GOBACK,SEG7PORT        ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 1 sec

JSR     WAIT            ;

LDX     #HARDLEFT       ; load manuever

MOVB    #HARDLEFT,SEG7PORT      ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 10 sec

JSR     WAIT            ;

LDX     #SOFTLEFT       ; load manuever

MOVB    #SOFTLEFT,SEG7PORT      ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 1 sec

JSR     WAIT            ;

LDX     #HARDRIGHT      ; load manuever

MOVB    #HARDRIGHT,SEG7PORT     ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 10 sec

JSR     WAIT            ;

LDX     #SOFTRIGHT      ; load manuever

MOVB    #SOFTRIGHT,SEG7PORT     ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 1 sec

JSR     WAIT            ;

LDX     #STOP           ; load manuever

MOVB    #STOP,SEG7PORT          ; write direction to port

JSR     STEER           ; move the robot

LDX     #5000           ; wait 1 sec

JSR     WAIT            ;

BRA     TEST1

SWI

OLEFTSPD        DC.W    $0000           ; current speed of left motor

NLEFTSPD        DC.W    $0000           ; next speed of left motor

ORIGHTSPD       DC.W    $0000           ; current speed of right motor

NRIGHTSPD       DC.W    $0000           ; next speed of right motor

MAXFOWARDSPD    DC.W    $0000           ; maximum foward speed for motors

MAXBACKSPD      DC.W    $0000           ; maximum reverse speed for motors

CURRMAN         DC.W    $0000           ; current manuever being performed

#include "wait.asm"

#endif

*

*******************************************************************************

*                       SUBROUTINE -  INITPWM

* Description: Initializes the pulse width modulation system

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

INITPWM     MOVB    #$08,PWCLK          ; set prescaler bits, concatenate PWM channels

MOVB    #$33,PWPOL          ; set clock source (S0,S1), polarity (high first)

MOVB    #99,PWSCAL0         ; set S0 clock prescaler

MOVB    #$00,PWSCAL1        ; init S1 clock prescaler

MOVB    #200,PWPER0         ; set period of PWM0 to about 20ms

MOVB    #200,PWPER1         ; set period of PWM1 to about 20ms

MOVB    #$FF,PWPER2         ; init period of PWM2

MOVB    #$FF,PWPER3         ; init period of PWM3

MOVB    #$00,PWDTY0         ; init duty cycle to 0%

MOVB    #$00,PWDTY1         ; init duty cycle to 0%

MOVB    #$00,PWDTY2         ; init duty cycle to 0%

MOVB    #$00,PWDTY3         ; init duty cycle to 0%

MOVB    #$00,PWCTL          ; init PWM to run normally, left aligned

MOVB    #$50,DDRP           ; configure unused bits to be outputs (motor controls)

MOVB    #$50,PORTP          ; set direction to foward, brake to off

MOVB    #$03,PWEN           ; enable the PWM channels

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  KILLPWM

* Description: Shuts down the pulse width modulation system

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

KILLPWM     MOVB    #$00,PWEN           ; turn off PWM channels

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  LEFTMOTOR

* Description: Sets the left motor to the speed specified.  Valid

*               speed values range from -100 to 100, where 0 to -100 is back-

*               wards speed and 0 to 100 is foward speed.

*

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

LEFTMOTOR   PSHX                        ; save reg X

PSHY                        ; save reg Y

PSHD                        ; save reg D

LDD     OLEFTSPD            ; load the old speed

LDY     #ACCELCONST         ; get the acceleration constant

EMULS                       ; multiply old speed by acceleration constant

ADDD    NLEFTSPD            ; add new speed to result

LDX     #(ACCELCONST+1)     ; load divisor

IDIVS                       ; calc new speed

XGDX                        ; put new speed in reg D

STD     OLEFTSPD            ; save new speed as old speed

BLT     LEFTMOTOR1          ; if new speed is negative, branch

BSET    PORTP,LEFTDIR       ; set direction to foward

BRA     LEFTMOTOR2          ; continue

LEFTMOTOR1  BCLR    PORTP,LEFTDIR       ; set direction to reverse

NEGB                        ; take abs value of speed

LEFTMOTOR2  STAB    PWDTY1              ; set the new speed for the left motor

PULD                        ; restore reg D

PULY                        ; restore reg Y

PULX                        ; restore reg X

LEFTMOTORX  RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  RIGHTMOTOR

* Description: Sets the right motor to the speed specified.  Valid

*               speed values range from -100 to 100, where 0 to -100 is back-

*               wards speed and 0 to 100 is foward speed.

*

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

RIGHTMOTOR  PSHX                        ; save reg X

PSHY                        ; save reg Y

PSHD                        ; save reg D

LDD     ORIGHTSPD           ; load the old speed

LDY     #ACCELCONST         ; get the acceleration constant

EMULS                       ; multiply old speed by acceleration constant

ADDD    NRIGHTSPD           ; add new speed to result

LDX     #(ACCELCONST+1)     ; load divisor

IDIVS                       ; calc new speed

XGDX                        ; put new speed in reg D

STD     ORIGHTSPD           ; save new speed as old speed

BLT     RIGHTMOTOR1         ; if new speed is negative, branch

BSET    PORTP,RIGHTDIR      ; set direction to foward

BRA     RIGHTMOTOR2         ; continue

RIGHTMOTOR1 BCLR    PORTP,RIGHTDIR      ; set direction to reverse

NEGB                        ; take abs value of speed

RIGHTMOTOR2 STAB    PWDTY0              ; set the new speed for the right motor

PULD                        ; restore reg D

PULY                        ; restore reg Y

PULX                        ; restore reg X

RIGHTMOTORX RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  CHNGSPEED

* Description: Changes the maximum speed for either motor to the speed passed

*               in register D.

* Input         : Speed(reg D).

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

CHNGSPEED   STD     MAXFOWARDSPD        ; save max speed

STD     MAXBACKSPD          ; save max speed to backward

COM     MAXBACKSPD          ; convert to negative speed

NEG     MAXBACKSPD+1        ;

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  STEER

* Description: Sets up the left and right motors to perform the specified

*               manuever (reg X). The value of manuever must be one of the

*               following:

*

*                   GOFOWARD

*                   GOBACK

*                   HARDLEFT

*                   SOFTLEFT

*                   HARDRIGHT

*                   SOFTRIGHT

*                   BACKLEFT

*                   BACKRIGHT

*                   STOP

*

* Input         : Manuever(reg X).

* Output        : None.

* Destroys      : None.

* Calls         : LEFTMOTOR,RIGHTMOTOR.

*******************************************************************************

*

STEER       PSHD                            ; save register D

PSHX                            ; save register X

STX     CURRMAN                 ; save manuever

TBNE    X,STEER1                ; if not FOWARD, continue

LDD     MAXFOWARDSPD            ; load maximum foward speed

STD     NRIGHTSPD               ; right motor full foward

STD     NLEFTSPD                ; left motor foward full

BRA     STEERX                  ; get out

STEER1      DBNE    X,STEER2                ; if not BACKWARD, continue

LDD     MAXBACKSPD              ; load maximum back speed

STD     NRIGHTSPD               ; right motor back full

STD     NLEFTSPD                ; left motor back full

BRA     STEERX                  ; get out

STEER2      DBNE    X,STEER3                ; if not HARD LEFT, continue

LDD     MAXFOWARDSPD            ; load maximum foward speed

STD     NRIGHTSPD               ; right motor foward full

LDD     MAXBACKSPD              ; load maximum back speed

STD     NLEFTSPD                ; left motor backward full

BRA     STEERX                  ; get out

STEER3      DBNE    X,STEER4                ; if not SOFT LEFT, continue

LDD     MAXFOWARDSPD            ; load maximum foward speed

STD     NRIGHTSPD               ; right motor foward full

LSRD                            ; set left motor speed

STD     NLEFTSPD                ; left motor foward half

BRA     STEERX                  ; get out

STEER4      DBNE    X,STEER5                ; if not HARD RIGHT, continue

LDD     MAXFOWARDSPD            ; load maximum foward speed

STD     NLEFTSPD                ; left motor foward full

LDD     MAXBACKSPD              ; load maximum back speed

STD     NRIGHTSPD               ; right motor back full

BRA     STEERX                  ; get out

STEER5      DBNE    X,STEER6                ; if not SOFT RIGHT, continue

LDD     MAXFOWARDSPD            ; load maximum foward speed

STD     NLEFTSPD                ; left motor foward full

LSRD                            ; set right motor speed

STD     NRIGHTSPD               ; right motor foward half

BRA     STEERX                  ; get out

STEER6      DBNE    X,STEER7                ; if not BACK LEFT, continue

LDD     MAXBACKSPD              ; load maximum foward speed

STD     NRIGHTSPD               ; right motor back full

LSRD                            ; set left motor speed

STD     NLEFTSPD                ; left motor foward half

BRA     STEERX                  ; get out

STEER7      DBNE    X,STEER8                ; if not BACK RIGHT, continue

LDD     MAXBACKSPD              ; load maximum foward speed

STD     NLEFTSPD                ; left motor back full

LSRD                            ; set left motor speed

STD     NRIGHTSPD               ; right motor foward half

BRA     STEERX                  ; get out

STEER8      DBNE    X,STEERX                ; if not STOP, get out

MOVW    #$0000,NLEFTSPD         ; stop left motor

MOVW    #$0000,NRIGHTSPD        ; stop right motor

STEERX      PULX                            ; restore register X

PULD                            ; restore register D

RTS                             ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  PULLOUT

* Description: Performs pre-programmed manuever to pull out onto the road and

*               turn toward moving objext to begin chasing

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

PULLOUT     PSHD                        ; save reg D

PSHX                        ; save reg X

LDD     #FULLSPEED          ; set motor speed

JSR     CHNGSPEED           ;

LDX     #GOFOWARD           ; pull foward

JSR     STEER               ;

LDX     #60                 ; for a little bit

JSR     WAIT                ;

LDAA    SPDCAUGHT           ; get direction of speeder

CMPA    #LSPDFLAG           ; was the speeder going left?

BEQ     PULLOUTL            ; yes, so go pull out left

PULLOUTR

LDX     #SOFTRIGHT          ; no, then pull out right

JSR     STEER               ;

LDX     #625                ; wait for manuever

JSR     WAIT                ;

BRA     PULLOUTX            ; get out

PULLOUTL

LDX     #SOFTLEFT           ; turn left

JSR     STEER               ;

LDX     #600                ; wait for manuever

JSR     WAIT                ;

PULLOUTX    PULX                        ; restore reg X

PULD                        ; restore reg D

RTS                         ; return to caller

*

*******************************************************************************

* Filename      : TIME.ASM

* Programmer    : Michael Hattermann

* Date          : February 21, 2002

* Version       : 1.0

* Description   : This file contains time functions.  The

*                  following functions are available:

*

*                   INITTIME - initialize timer system

*                   KILLTIME - shut down timer system

*                   WAITSPEED - waits for a speeder to go by

*                   FLASHON - turns on flashing lights

*                   FLASHOFF - turns off flashing lights

*                   SIRENON - turns on the siren

*                   SIRENOFF - turns off the siren

*                   LEFTSTS - handles left speed trap sensor

*                   RIGHTSTS - handles right speed trap sensor

*                   TIMEEXT - handles extended timer,flashing lights,siren

*                   UPDMOTORS - updates speed on motors

*                   SIREN - handles siren output

*

*#define __DEBUGTIME_        1

*#define __PRINTTIME_        1

#include "hc12.asm"

*

************************************************************

* Time Equates

************************************************************

*

LSPDFLAG        EQU         BIT0    ; Flags to indicate if a

RSPDFLAG        EQU         BIT1    ;  beam was broken

BSPDFLAG        EQU         3       ;

SPDLIMIT        EQU         $1F     ; speed limit

FLASHRATE       EQU         15      ; flashing light rate (1/4 second)

FLASHPAT1       EQU         $0F     ; 1st light pattern

FLASHPAT2       EQU         $F0     ; 2nd light pattern

SIRENRATE1      EQU         -10     ; siren frequency change rate

SIRENRATE2      EQU         10      ; siren frequency change rate

SIRENFREQ1      EQU         2000    ; first siren frequency

SIRENFREQ2      EQU         1200    ; second siren frequency

*

************************************************************

* Time Debug Program

************************************************************

*

#ifdef  __DEBUGTIME_

ORG     T0_PVECT

JMP     LEFTSTS

ORG     T1_PVECT

JMP     RIGHTSTS

ORG     TMR_OVER_PVECT

JMP     TIMEEXT

ORG     RTI_PVECT

JMP     UPDMOTORS

ORG     T6_PVECT

JMP     SIREN

*

************************************************************

* Time Global Vairables

************************************************************

*

ORG     $0900

UPPERTIMER      DC.W    $0000           ; 16-bit extension of TCNT

LEFTSPDTIME     DC.W    $0000           ; Time left break beam was broken

RIGHTSPDTIME    DC.W    $0000           ; Time right break beam was broken

SPDTIMEFLG      DC.B    $00             ; Flags to indicate which beams were broken

SPDCAUGHT       DC.B    $00             ; Flags to indicate speeder caught

FLASHTIMER      DC.B    $00             ; Timer for flashing lights

FLASHPREV       DC.B    $00             ; Previous status of lights

SIRENFREQ       DC.W    $0000           ; Frequency of the siren

SIRENTIMER      DC.W    $0000           ; Timer for siren

ORG     USERPROG_PVECT

JMP     TEST

ORG     $B000

TEST        LDAA    #$00            ; turn off COP watchdog timer

STAA    COPCTL

LDS     #$0bff          ; init the stack pointer

JSR     INITTIME        ; initialize the time system

*            LDX     #0              ; wait 0 ms

*            JSR     WAIT            ;

*            LDX     #1              ; wait 1 ms

*            JSR     WAIT            ;

*            LDX     #10             ; wait 10 ms

*            JSR     WAIT            ;

CLI                     ; turn on interrupts

JSR     FLASHON         ;

*            JSR     SIRENON

HERE        BRA     HERE            ; end of program

LEFTMOTOR       RTS

RIGHTMOTOR      RTS

LEFTSPSTR   DC.B    'L'

DC.B    CR,LF,EOS

RIGHTSPSTR  DC.B    'R'

DC.B    CR,LF,EOS

NEWLINE     DC.B    CR,LF,EOS

#include "sci.asm"

*#include "wait.asm"

#endif

*

*******************************************************************************

*                       SUBROUTINE -  INITTIME

* Description: Initializes the timer system

*               TC0     - left speed trap IR receiver

*               TC1     - right speed trap IR receiver

*               TC6     - siren output

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

INITTIME    MOVB    #$40,TIOS           ; setup input capture/output compare lines

MOVB    #$00,CFORC          ; setup timer compare force register

MOVB    #$00,OC7M           ; setup OC7 mask register

MOVB    #$00,OC7D           ; setup OC7 data register

MOVB    #$00,TCTL1          ; setup output compare pin action reg 1

MOVB    #$00,TCTL2          ; setup output compare pin action reg 2

MOVB    #$00,TCTL3          ; setup input capture edge detection reg 1

MOVB    #$05,TCTL4          ; setup input capture edge detection reg 2

MOVB    #$03,TMSK1          ; setup interrupts on timer lines

MOVB    #$A0,TMSK2          ; setup misc timer pin options(pullups on IC pins)

MOVW    #$0000,TC0          ; clear TC0 register

MOVW    #$0000,TC1          ; clear TC1 register

MOVW    #$0000,TC2          ; clear TC2 register

MOVW    #$0000,TC3          ; clear TC3 register

MOVW    #$0000,TC4          ; clear TC4 register

MOVW    #$0000,TC5          ; clear TC5 register

MOVW    #$0000,TC6          ; clear TC6 register

MOVW    #$0000,TC7          ; clear TC7 register

MOVB    #$FF,TFLG1          ; clear all interrupt flags

MOVB    #$80,TFLG2          ; clear interrupt flag

MOVW    #$0000,UPPERTIMER   ; clear timer extension timer

MOVW    #$0000,LEFTSPDTIME  ; clear left speed time

MOVW    #$0000,RIGHTSPDTIME ; clear left speed time

MOVB    #$00,FLASHTIMER     ; clear flashing lights timer

MOVB    #$00,SPDTIMEFLG     ; clear broken beam flags

MOVB    #$00,SPDCAUGHT      ; clear speeder caught flag

MOVB    #$00,FLASHPREV      ; turn off flashing lights

MOVW    #$0000,SIRENFREQ    ; clear siren frequency

MOVW    #$0000,SIRENTIMER   ; clear siren timer

MOVB    #$00,BUMPVALUE      ; clear bumper value

MOVB    #$86,RTICTL         ; set up, enable RTI

MOVB    #$FF,RTIFLG         ; clear all RTI flags

MOVB    #$80,TSCR           ; enable the timer

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  KILLTIME

* Description: Shuts down the timer system

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

KILLTIME    MOVB    #$00,TCTL1          ; disconnect all output compare pins

MOVB    #$00,TCTL2          ;

MOVB    #$00,TCTL3          ; disable all input capture pins

MOVB    #$00,TCTL4          ;

MOVB    #$00,TMSK1          ; turn off interrupts

MOVB    #$00,TMSK2          ; turn off timer overflow interrupts

MOVB    #$00,PACTL          ; turn off pulse accumulator

MOVB    #$00,TSCR           ; turn off timer

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  WAITSPEED

* Description: Waits for a speeder to be caught and returns the direction the

*               object was travelling (Reg A).  Valid values are:

*                    LSPDFLAG - object was going left

*                    RSPDFLAG - object was going right

*

* Input         : None.

* Output        : Direction in reg A.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

WAITSPEED

WAITSPEED1  LDAA    SPDCAUGHT       ; get flags for speeder caught

TBEQ    A,WAITSPEED1    ; wait for a caught speeder

BCLR    TMSK1,#BIT0     ; turn off left interrupts

BCLR    TMSK1,#BIT0     ; turn off right interrupts

RTS                     ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  FLASHON

* Description: Turns the flashing lights on

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

FLASHON     MOVB    #FLASHPAT1,FLASHPREV    ; turn on the lights

RTS                             ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  FLASHOFF

* Description: Turns the flashing lights off

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

FLASHOFF    MOVB    #$00,FLASHPREV          ; turn off the lights

RTS                             ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  SIRENON

* Description: Turns the siren on

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

SIRENON     MOVB    #$10,TCTL1              ; turn on pin action for siren

BSET    TMSK1,#BIT6              ; turn on interrupts for siren

MOVW    #SIRENFREQ1,SIRENFREQ   ; initialize the siren frequency

MOVW    #SIRENRATE1,SIRENTIMER  ; start going up in frequency first

RTS                             ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  SIRENOFF

* Description: Turns the siren off

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

SIRENOFF    BCLR    TMSK1,#BIT6              ; turn off interrupts for siren

MOVB    #$00,TCTL1              ; turn off pin action for siren

MOVW    #$0000,SIRENFREQ        ; clear siren frequency

RTS                             ; return to caller

*

*******************************************************************************

*                 INTERRUPT SERVICE ROUTINE - LEFTSTS

* Description: Handles the processing for a signal received from the left

*               speed trap sensor.

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

LEFTSTS     BRCLR   TFLG1,BIT0,LEFTSTSX     ; make sure we should be here

MOVB    #BIT0,TFLG1             ; clear the flag

#ifdef __PRINTTIME_

PSHX                            ; save reg X

LDX     #LEFTSPSTR              ; print beam broken

JSR     OUTSTR                  ;

PULX                            ; restore X

#endif

MOVW    UPPERTIMER,LEFTSPDTIME  ; save time beam was broken

LDAA    SPDTIMEFLG              ; load flags for broken beams

ORAA    #LSPDFLAG               ; set the left flag

CMPA    #BSPDFLAG               ; have both beams been broken?

BEQ     LEFTSTS1                ; yes, then go handle

STAA    SPDTIMEFLG              ; no, save flags for borken beams

BRA     LEFTSTSX                ; get out

LEFTSTS1    MOVB    #$00,SPDTIMEFLG         ; clear flags for broken beams

LDD     LEFTSPDTIME             ; get the left beam broken time

CPD     RIGHTSPDTIME            ; did the timer roll over

BLO     LEFTSTS2                ; yes, so calc speed differently

SUBD    RIGHTSPDTIME            ; calculate time difference

BRA     LEFTSTS3

LEFTSTS2    LDD     RIGHTSPDTIME            ; load time right beam broken

SUBD    LEFTSPDTIME             ; calculate time difference

LEFTSTS3    CPD     #SPDLIMIT               ; was the object speeding?

BHS     LEFTSTS4                ; no, so get out

MOVB    #LSPDFLAG,SPDCAUGHT     ; yes, set flag for speeder caught

LEFTSTS4    COMB                            ;

STAB    SEG7PORT                ; write speed to port

LEFTSTSX    RTI                             ; return from interrupt

*

*******************************************************************************

*                 INTERRUPT SERVICE ROUTINE - RIGHTSTS

* Description: Handles the processing for a signal received from the right

*               speed trap sensor.

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

RIGHTSTS    BRCLR   TFLG1,BIT1,RIGHTSTSX    ; make sure we should be here

MOVB    #BIT1,TFLG1             ; clear the flag

#ifdef __PRINTTIME_

PSHX                            ; save reg X

LDX     #RIGHTSPSTR             ; print beam broken

JSR     OUTSTR                  ;

PULX                            ; restore reg X

#endif

MOVW    UPPERTIMER,RIGHTSPDTIME ; save time beam was broken

LDAA    SPDTIMEFLG              ; load flags for broken beams

ORAA    #RSPDFLAG               ; set the right flag

CMPA    #BSPDFLAG               ; have both beams been broken?

BEQ     RIGHTSTS1               ; yes, then go handle

STAA    SPDTIMEFLG              ; no, save flags for borken beams

BRA     RIGHTSTSX               ; get out

RIGHTSTS1   MOVB    #$00,SPDTIMEFLG         ; clear flags for broken beams

LDD     RIGHTSPDTIME            ; get the right beam broken time

CPD     LEFTSPDTIME             ; did the timer roll over

BLO     RIGHTSTS2               ; yes, so calc speed differently

SUBD    LEFTSPDTIME             ; calculate time difference

BRA     RIGHTSTS3

RIGHTSTS2   LDD     LEFTSPDTIME             ; load time right beam broken

SUBD    RIGHTSPDTIME            ; calculate time difference

RIGHTSTS3   CPD     #SPDLIMIT               ; was the object speeding?

BHS     RIGHTSTS4               ; no, so get out

MOVB    #RSPDFLAG,SPDCAUGHT     ; yes, set flag for speeder caught (going right)

RIGHTSTS4   COMB                            ;

STAB    SEG7PORT                ; write speed to port

RIGHTSTSX   RTI                             ; return from interrupt

*

*******************************************************************************

*                 INTERRUPT SERVICE ROUTINE - TIMEEXT

* Description: Increments the extended timer when a timer overflow occurs in

*               TCNT (it is incremented every 8ms).

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

TIMEEXT     BRCLR   TFLG2,BIT7,TIMEEXTX     ; make sure we should be here

MOVB    #BIT7,TFLG2             ; clear the flag

LDX     UPPERTIMER              ; get the timer extension

INX                             ; increment the timer extension

STX     UPPERTIMER              ; save the timer extension

LDD     SIRENFREQ               ; get previous siren frequency

BEQ     TIMEEXT2                ; if siren off, keep it off

ADDD    SIRENTIMER              ; update siren frequency

STD     SIRENFREQ               ; save siren frequency

CPD     #SIRENFREQ1             ; are we at low end of range

BLO     TIMEEXT1                ; no, continue

MOVW    #SIRENRATE1,SIRENTIMER  ; yes, so start going back up

BRA     TIMEEXT2                ; continue

TIMEEXT1    CPD     #SIRENFREQ2             ; are we at high end of range

BHI     TIMEEXT2                ; no, continue

MOVW    #SIRENRATE2,SIRENTIMER   ; yes, so start going down

TIMEEXT2    LDAB    FLASHPREV               ; get previous status of lights

BEQ     TIMEEXTX                ; if lights off, keep them off

LDAA    FLASHTIMER              ; get the flashing lights timer

INCA                            ; increment the timer

STAA    FLASHTIMER              ; save flashing lights timer

CMPA    #FLASHRATE              ; do we need to change light status

BNE     TIMEEXTX                ; no, so get out

COMB                            ; switch light pattern

STAB    FLASHPREV               ; save new light pattern

STAB    LED1PORT                ; turn on lights with new pattern

MOVB    #$00,FLASHTIMER         ; reset flashing lights timer

TIMEEXTX    RTI                             ; return from interrupt

*

*******************************************************************************

*                 INTERRUPT SERVICE ROUTINE - UPDMOTORS

* Description: Updates the speed of the motors on every RTI interrupt

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

UPDMOTORS   BRCLR   RTIFLG,BIT7,UPDMOTORSX      ; make sure we should be here

MOVB    #BIT7,RTIFLG                ; clear the flag

JSR     LEFTMOTOR                   ; update speed on left motor

JSR     RIGHTMOTOR                  ; update speed on right motor

UPDMOTORSX  RTI                                 ; return from interrupt

*

*******************************************************************************

*                 INTERRUPT SERVICE ROUTINE - SIREN

* Description: Handles generating the frequency of the siren

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

SIREN       BRCLR   TFLG1,BIT6,SIRENX           ; make sure we should be here

MOVB    #BIT6,TFLG1                 ; clear the flag

LDD     TC6                         ; get previous interrupt time

ADDD    SIRENFREQ                   ; calc next time (set frequency of siren)

STD     TC6                         ; set next interrupt time

SIRENX      RTI                                 ; return from interrupt

*

*******************************************************************************

* Filename      : WAIT.ASM

* Programmer    : Michael Hattermann

* Date          : March 29, 2002

* Version       : 1.0

* Description   : This file contains the wait and bumper

*                 functions. They must be together because

*                 the bumpers are checked while waiting. The

*                 following functions are available:

*

*                   WAIT - waits for specified # ms

*                   BUMPED - Determines if a bump has occured

*

*#define __DEBUGBUMP_    1

#define __PRINTBUMP_    1

#include "hc12.asm"

*

************************************************************

* Bump/Wait Equates

************************************************************

*

NOBUMPMAX       EQU     $09             ; max value for no bumper pressed

FRONTREAR       EQU     $47             ; division between front and back

*

************************************************************

* Bump/Wait Debug Code

************************************************************

*

#ifdef __DEBUGBUMP_

ORG     USERPROG_PVECT

JMP     TEST

ORG     $0900

BUMPVALUE   DC.B    $00             ; bumper value

ORG     $B000

TEST        LDAA    #$00            ; turn off COP watchdog timer

STAA    COPCTL

LDS     #$0bff          ; init the stack pointer

LDX     #1000           ;

JSR     WAIT            ;

JSR     INITATD         ; init A/D system

JSR     INITSCI         ; init SCI system

MOVB    #$80,TSCR       ; enable the timer

TEST1       LDX     #500            ; wait 1/2 sec

JSR     WAIT            ;

LDAA    BUMPVALUE       ; get bumper value

TBEQ    A,TEST1         ; if bumper not pressed, keep checking

BRA     TEST1           ;

TEST2       LDX     #1              ; wait 1ms to time wait routine

LDY     TCNT            ; get start value of timer

JSR     WAIT            ; wait

LDX     TCNT            ; get end value of timer

JSR     OUTADDR         ; print start value

LDAA    #$20            ; print blank space

JSR     OUTCHAR         ;

TFR     Y,X             ; get end value

JSR     OUTADDR         ; print end value

LDX     #NEWLINE        ; print end of line

JSR     OUTSTR          ;

BRA     TEST1           ;

NEWLINE     DC.B    CR,LF,EOS

#include "sci.asm"

#include "atd.asm"

#endif

#ifdef __PRINTBUMP_

BUMPSTR     DC.B    'BUMPER VALUE = '

DC.B    EOS

#endif

*

*******************************************************************************

*                       SUBROUTINE -  WAIT

* Description: Waits for the designated amount of time (in ms).  If a bumper is

*               pressed while waiting, it will quit waiting and returns to the

*               function that called it. Function returns 0 if waited full time,

*               returns bumper value otherwise

* Input         : # of ms to wait in reg X.

* Output        : Bumper value in BUMPVALUE.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

WAIT        TBEQ    X,WAITX         ; if no time to wait, get out

PSHX                    ; save reg X

PSHD                    ; save reg D

MOVB    #$00,BUMPVALUE  ; clear old bumper value

WAIT1       LDAB    #11             ; load loop counter

WAIT2       LDAA    #BUMPER         ; check to see if we have

JSR     ANALOG          ;   been bumped

CMPA    #NOBUMPMAX      ; were we bumped?

BHI     WAITBX          ; yes, get out

NOP                     ; do nothing

NOP                     ;

NOP                     ;

NOP                     ;

NOP                     ;

NOP                     ;

NOP                     ;

NOP                     ;

NOP                     ;

DBNE    B,WAIT2         ; repeat until counter=0

DBNE    X,WAIT1         ; if we need to wait more, go wait

WAITX       PULD                    ; restore reg D

PULX                    ; restore reg X

RTS                     ; return to caller

WAITBX      STAA    BUMPVALUE       ; save bumper value

#ifdef __PRINTBUMP_

PSHX                    ; save reg X

LDX     #BUMPSTR        ; print bump string

JSR     OUTSTR          ;

JSR     OUTNUM          ; print analog value

LDX     #NEWLINE        ; print end of line

JSR     OUTSTR          ;

PULX                    ; restore reg X

#endif

BRA     WAITX           ; get out

*******************************************************************************

*                       SUBROUTINE -  BUMPED

* Description: Determines if a bump sensor has been pressed.  If it has, the

*               function will return the value read from the bumper A/D port.

*               If no bumper is pressed, a $00 will be returned.

* Input         : None.

* Output        : Bumper value in reg A.

* Destroys      : Reg A.

* Calls         : None.

*******************************************************************************

*

BUMPED      LDAA    BUMPVALUE           ; get the last bump value

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  WAIT

* Description: Waits for the designated amount of time (in ms).

* Input         : # of ms to wait in reg X.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

*WAIT        TBEQ    X,WAITX         ; if no time to wait, get out

*            PSHX                    ; save reg X

*            PSHD                    ; save reg D

*

*WAIT1       LDD    #1323            ; load loop counter

*

*WAIT2

*            DBNE    D,WAIT2         ; repeat until counter=0

*

*            DBNE    X,WAIT1         ; if we need to wait more, go wait

*

*WAITX       PULD                    ; restore reg D

*            PULX                    ; restore reg X

*            RTS                     ; return to caller

*

*******************************************************************************

* Filename      : OBJAVOID.ASM

* Programmer    : Michael Hattermann

* Date          : February 4, 2002

* Version       : 1.0

* Description   : This file contains the code for

*                 object avoidance. The following

*                 functions are available:

*

*                   OBJAVOID - reads IR and avoids obstacles

*                   GETVALUES - reads IR values from analog port

*                   CONVREACT - converts IR value to a reaction

*                   LEFTRIGHT - decided to turn left,right,or random

*                   BACKUP - backs robot up and turns it

*                   HARD - turns robot hard in a direction

*                   SOFT - turns robot soft in a direction

*

*

*#define __DEBUGOBJAVOID2_ 1

*#define __PRINTOBJAVOID2_ 1

#include "hc12.asm"

*

************************************************************

* Object Avoidance Equates

************************************************************

*

LREQUAL         EQU         $10         ; left,right IR values equality threshold

BACKUPTIME      EQU         150         ; # ms to backup

*

************************************************************

* OBJAVOID2 Debug Code

************************************************************

*

#ifdef __DEBUGOBJAVOID2_

ORG     USERPROG_PVECT

JMP     TEST

ORG     $B000

TEST        JSR     INITATD         ; init A/D system

TEST1       LDAA    #HALFSPEED      ; go at half speed

JSR     OBJAVOID        ; go avoid objects

BRA     TEST1

SWI

LVALUE      DC.B        $00         ; value of left IR

LREACT      DC.B        $00         ; reaction to left IR value

RVALUE      DC.B        $00         ; value of right IR

RREACT      DC.B        $00         ; reaction to right IR value

CVALUE      DC.B        $00         ; value of center IR

CREACT      DC.B        $00         ; reaction to center IR value

PREVRAND    DC.B        $00         ; previous turn direction

PREVREACT   DC.B        $00         ; previous reaction value

#include "atd.asm"

#include "time.asm"

#include "pwm.asm"

#include "sci.asm"

#include "wait.asm"

#endif

#ifdef __PRINTOBJAVOID2_

LEFT        DC.B    'Left IR='

DC.B    EOS

CENTER      DC.B    ', Center IR='

DC.B    EOS

RIGHT       DC.B    ', Right IR='

DC.B    EOS

LEFTR       DC.B    'Left Reaction='

DC.B    EOS

CENTERR     DC.B    ', Center Reaction='

DC.B    EOS

RIGHTR      DC.B    ', Right Reaction='

DC.B    EOS

BACKSTR     DC.B    'BACKUP'

DC.B    CR,LF,CR,LF,EOS

LHARDSTR    DC.B    'HARD LEFT'

DC.B    CR,LF,CR,LF,EOS

LSOFTSTR    DC.B    'SOFT LEFT'

DC.B    CR,LF,CR,LF,EOS

RHARDSTR    DC.B    'HARD RIGHT'

DC.B    CR,LF,CR,LF,EOS

RSOFTSTR    DC.B    'SOFT RIGHT'

DC.B    CR,LF,CR,LF,EOS

FOWARDSTR   DC.B    'FOWARD'

DC.B    CR,LF,CR,LF,EOS

#endif

* Reaction table for values for center IR

************************************************************

CNTRTBL     DC.B        NOACTION        ; $00-$07

DC.B        NOACTION        ; $08-$0F

DC.B        NOACTION        ; $10-$17

DC.B        NOACTION        ; $18-$1F

DC.B        REACTSOFT       ; $20-$27

DC.B        REACTSOFT       ; $28-$2F

DC.B        REACTSOFT       ; $30-$37

DC.B        REACTSOFT       ; $38-$3F

DC.B        REACTSOFT       ; $40-$47

DC.B        REACTHARD       ; $48-$4F

DC.B        REACTHARD       ; $50-$57

DC.B        REACTHARD       ; $58-$5F

DC.B        REACTHARD       ; $60-$67

DC.B        REACTHARD       ; $68-$6F

DC.B        REACTBACK       ; $70-$77

DC.B        REACTBACK       ; $78-$7F

DC.B        REACTBACK       ; $80-$87

DC.B        REACTBACK       ; $88-$8F

DC.B        REACTBACK       ; $90-$97

DC.B        REACTBACK       ; $98-$9F

* Reaction table for values for left,right IR

************************************************************

LEFTTBL     DC.B        NOACTION        ; $00-$07

DC.B        NOACTION        ; $08-$0F

DC.B        NOACTION        ; $10-$17

DC.B        NOACTION        ; $18-$1F

DC.B        REACTSOFT       ; $20-$27

DC.B        REACTSOFT       ; $28-$2F

DC.B        REACTSOFT       ; $30-$37

DC.B        REACTSOFT       ; $38-$3F

DC.B        REACTHARD       ; $40-$47

DC.B        REACTHARD       ; $48-$4F

DC.B        REACTHARD       ; $50-$57

DC.B        REACTHARD       ; $58-$5F

DC.B        REACTHARD       ; $60-$67

DC.B        REACTHARD       ; $68-$6F

DC.B        REACTBACK       ; $70-$77

DC.B        REACTBACK       ; $78-$7F

DC.B        REACTBACK       ; $80-$87

DC.B        REACTBACK       ; $88-$8F

DC.B        REACTBACK       ; $90-$97

DC.B        REACTBACK       ; $98-$9F

* Reaction table for values for left,right IR

************************************************************

RIGHTTBL    DC.B        NOACTION        ; $00-$07

DC.B        NOACTION        ; $08-$0F

DC.B        NOACTION        ; $10-$17

DC.B        NOACTION        ; $18-$1F

DC.B        REACTSOFT       ; $20-$27

DC.B        REACTSOFT       ; $28-$2F

DC.B        REACTSOFT       ; $30-$37

DC.B        REACTSOFT       ; $38-$3F

DC.B        REACTHARD       ; $40-$47

DC.B        REACTHARD       ; $48-$4F

DC.B        REACTHARD       ; $50-$57

DC.B        REACTHARD       ; $58-$5F

DC.B        REACTHARD       ; $60-$67

DC.B        REACTHARD       ; $68-$6F

DC.B        REACTBACK       ; $70-$77

DC.B        REACTBACK       ; $78-$7F

DC.B        REACTBACK       ; $80-$87

DC.B        REACTBACK       ; $88-$8F

DC.B        REACTBACK       ; $90-$97

DC.B        REACTBACK       ; $98-$9F

*

*******************************************************************************

*                       SUBROUTINE -  OBJAVOID

* Description: Performs an obstacle avoidance behavior by reading the values

*               from the IR and bump sensors and moving the robot accordingly.

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : GETVALUES,CONVREACT.

*******************************************************************************

*

OBJAVOID    PSHD                    ; save reg D

PSHX                    ; save reg X

JSR     BUMPED          ; check to see if we bumped something

CMPA    #FRONTREAR      ; did we bump something in the front?

BLO     OBJAVOIDB       ; no bump, check the IR

JMP     BACKUP          ; we bumped something, backup

OBJAVOIDB   JSR     GETVALUES       ; get the IR readings

JSR     CONVREACT       ; convert readings to reactions

LDAB    #REACTBACK      ; get code for back up reaction

CMPB    CREACT          ; does center say backup

BNE     OBJAVOID1       ; no, continue checking

JMP     BACKUP          ; yes, backup

OBJAVOID1   CMPB    LREACT          ; does left say backup

BNE     OBJAVOID2       ; no, continue checking

JMP     BACKUP          ; yes, backup

OBJAVOID2   CMPB    RREACT          ; does right say backup

BNE     OBJAVOID3       ; no, continue checking

JMP     BACKUP          ; yes, backup

OBJAVOID3   LDAB    #REACTHARD      ; get code for hard turn reaction

CMPB    CREACT          ; does center say backup

BNE     OBJAVOID4       ; no, continue checking

JMP     HARD            ; yes, turn hard

OBJAVOID4   CMPB    LREACT          ; does left say turn hard

BNE     OBJAVOID5       ; no, continue checking

JMP     HARD            ; yes, turn hard

OBJAVOID5   CMPB    RREACT          ; does right say turn hard

BNE     OBJAVOID6       ; no, continue checking

JMP     HARD            ; yes, turn hard

OBJAVOID6   LDAB    #REACTSOFT      ; get code for hard turn reaction

CMPB    CREACT          ; does center say backup

BNE     OBJAVOID7       ; no, continue checking

JMP     SOFT            ; yes, turn soft

OBJAVOID7   CMPB    LREACT          ; does left say turn hard

BNE     OBJAVOID8       ; no, continue checking

JMP     SOFT            ; yes, turn soft

OBJAVOID8   CMPB    RREACT          ; does right say turn hard

BNE     OBJAVOID9       ; no, continue checking

JMP     SOFT            ; yes, turn hard

OBJAVOID9

#ifdef __PRINTOBJAVOID2_

PSHX                    ; save reg X

LDX     #FOWARDSTR      ; print foward string

JSR     OUTSTR          ;

PULX                    ; restore reg X

#endif

OBJAVOID10  LDX     #GOFOWARD               ; no obstacles, go foward at set speed

JSR     STEER                   ;

CLR     PREVRAND                ; clear previous random direction

MOVB    #NOACTION,PREVREACT     ; save this reaction

OBJAVOIDX   PULX                    ; restore reg X

PULD                    ; restore reg D

RTS                     ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  GETVALUES

* Description: Gets the IR values for the left,center,and right channels

* Input         : None.

* Output        : RVALUE,LVALUE,CVALUE.

* Destroys      : RVALUE,LVALUE,CVALUE.

* Calls         : ANALOG.

*******************************************************************************

*

GETVALUES   PSHA                    ; save reg A

LDAA    #RIGHTIR        ; read right IR value

JSR     ANALOG          ;

STAA    RVALUE          ; save right IR value

LDAA    #LEFTIR         ; read left IR value

JSR     ANALOG          ;

STAA    LVALUE          ; save left IR value

LDAA    #CENTERIR       ; read center IR value

JSR     ANALOG          ;

STAA    CVALUE          ; save center IR value

#ifdef __PRINTOBJAVOID2_

PSHX                    ; save reg X

LDX     #LEFT           ; print left IR header

JSR     OUTSTR          ;

LDAA    LVALUE          ; print left IR value

JSR     OUTNUM          ;

LDX     #CENTER         ; print center IR header

JSR     OUTSTR          ;

LDAA    CVALUE          ; print center IR value

JSR     OUTNUM          ;

LDX     #RIGHT          ; print right IR header

JSR     OUTSTR          ;

LDAA    RVALUE          ; print right IR value

JSR     OUTNUM          ;

LDX     #NEWLINE        ; print new line

JSR     OUTSTR          ;

PULX                    ; restore reg X

#endif

PULA                    ; restore reg A

RTS                     ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  CONVREACT

* Description: Converts IR readings to reaction values using lookup tables

* Input         : RVALUE,LVALUE,CVALUE.

* Output        : CREACT,LREACT,RREACT.

* Destroys      : CREACT,LREACT,RREACT.

* Calls         : None.

*******************************************************************************

*

CONVREACT   PSHX                            ; save register X

LDX     #CNTRTBL                ; load address of lookup table

LDAB    CVALUE                  ; get center value

LSRB                            ; convert center value

LSRB                            ;  to table lookup

LSRB                            ;   value

MOVB    B,X,CREACT              ; lookup reaction for center

LDX     #LEFTTBL                ; load address of lookup table

LDAB    LVALUE                  ; get left value

LSRB                            ; convert left value

LSRB                            ;  to table lookup

LSRB                            ;   value

MOVB    B,X,LREACT              ; lookup reaction for left channel

LDX     #RIGHTTBL               ; load address of lookup table

LDAB    RVALUE                  ; get right value

LSRB                            ; convert right value

LSRB                            ;  to table lookup

LSRB                            ;   value

MOVB    B,X,RREACT              ; lookup reaction for right channel

#ifdef __PRINTOBJAVOID2_

PSHX                            ; save reg X

LDX     #LEFTR                  ; print left IR header

JSR     OUTSTR                  ;

LDAA    LREACT                  ; print left IR reaction

JSR     OUTNUM                  ;

LDX     #CENTERR                ; print center IR header

JSR     OUTSTR                  ;

LDAA    CREACT                  ; print center IR reaction

JSR     OUTNUM                  ;

LDX     #RIGHTR                 ; print right IR header

JSR     OUTSTR                  ;

LDAA    RREACT                  ; print right IR reaction

JSR     OUTNUM                  ;

LDX     #NEWLINE                ; print new line

JSR     OUTSTR                  ;

PULX                            ; restore reg X

#endif

PULX                            ; restore register X

RTS                             ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  LEFTRIGHT

* Description: Decides if we should turn left or right based on IR sensor

*               readings. It will compare left and right values, and if they

*               differ by more than some threshold, this decides the turn

*               direction.  Otherwise, turn direction is random.  Return values:

*                   REACTLEFT - Turn left

*                   REACTRIGHT - Turn right

* Input         : LVALUE,RVALUE.

* Output        : Reg B has direction.

* Destroys      : Reg B, PREVRAND.

* Calls         : None.

*******************************************************************************

*

LEFTRIGHT   PSHA                        ; save reg A

LDAA    LVALUE              ; get the left value

LDAB    RVALUE              ; get the right value

SBA                         ; compare the values

CMPA    #LREQUAL            ; if left > right by the threshold

BGE     LEFTRIGHT1          ; turn right

CMPA    #(-LREQUAL)         ; if left < right by the threshold

BLE     LEFTRIGHT2          ; turn left

TST     PREVRAND            ; do we have a previous direction

BEQ     LEFTRIGHTR          ; no, so go generate a direction

LDAB    PREVRAND            ; yes, so use previous direction

BRA     LEFTRIGHTX          ; get out

LEFTRIGHTR  LDAB    TCNTL               ; otherwise, get lower half of timer

LSRB                        ; check lowest bit

BCS     LEFTRIGHT2          ; go left if set, right if clear

LEFTRIGHT1  LDAB    #REACTRIGHT         ; turn right

STAB    PREVRAND            ; save previous direction

BRA     LEFTRIGHTX          ; get out

LEFTRIGHT2  LDAB    #REACTLEFT          ; turn left

STAB    PREVRAND            ; save previous direction

LEFTRIGHTX  PULA                        ; restore reg A

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  BACKUP

* Description: Backs up and turns a random direction (left or right).

* Input         : None.

* Output        : None.

* Destroys      : Reg B,Reg X,PREVRAND.

* Calls         : STEER,WAIT.

*******************************************************************************

*

BACKUP

MOVB    #REACTBACK,PREVREACT    ; save this reaction

CLR     PREVRAND                ; clear previous random direction

#ifdef __PRINTOBJAVOID2_

PSHX

LDX     #BACKSTR

JSR     OUTSTR

PULX

#endif

BACKUP1     JSR     LEFTRIGHT       ; do we have a preference left or right

CMPB    #REACTLEFT      ; if we need to go left, go left

BEQ     BACKUPL         ; go left

LDX     #BACKRIGHT      ; go hard right

JSR     STEER           ;

BRA     BACKUPX         ; get out

BACKUPL     LDX     #BACKLEFT       ; go hard left

JSR     STEER           ;

BACKUPX     LDX     #GOBACK         ; go backward

JSR     STEER           ;

LDX     #BACKUPTIME     ; go back for set amount of time

JSR     WAIT            ;

JMP     OBJAVOIDX       ; get out

*

*******************************************************************************

*                       SUBROUTINE -  HARD

* Description: Turns hard in a random direction (left or right).

* Input         : None.

* Output        : None.

* Destroys      : Reg B,Reg X.

* Calls         : STEER.

*******************************************************************************

*

HARD

LDAB    PREVREACT               ; get previous reaction

CMPB    #REACTHARD              ; was it react hard?

BEQ     HARD1                   ; yes, so continue

CLR     PREVRAND                ; no, clear previous turn direction

MOVB    #REACTHARD,PREVREACT    ; save this reaction

HARD1

JSR     LEFTRIGHT               ; do we have a preference left or right

CMPB    #REACTLEFT              ; if we need to go left, go left

BEQ     HARDL                   ; go left

#ifdef __PRINTOBJAVOID2_

PSHX                            ; save reg X

LDX     #RHARDSTR               ; print hard right string

JSR     OUTSTR                  ;

PULX                            ; restore reg X

#endif

HARDR       LDX     #HARDRIGHT              ; go hard right

JSR     STEER                   ;

JMP     OBJAVOIDX               ; get out

HARDL

#ifdef __PRINTOBJAVOID2_

PSHX                            ; save reg X

LDX     #LHARDSTR               ; print left hard string

JSR     OUTSTR                  ;

PULX                            ; restore reg X

#endif

LDX     #HARDLEFT               ; go hard left

JSR     STEER                   ;

JMP     OBJAVOIDX               ; get out

*

*******************************************************************************

*                       SUBROUTINE -  SOFT

* Description: Turns soft in a random direction (left or right).

* Input         : None.

* Output        : None.

* Destroys      : Reg B,Reg X.

* Calls         : STEER,WAIT.

*******************************************************************************

*

SOFT

LDAB    PREVREACT               ; get previous reaction

CMPB    #REACTSOFT              ; was it react soft?

BEQ     SOFT1                   ; yes, so continue

CLR     PREVRAND                ; no, clear previous turn direction

MOVB    #REACTSOFT,PREVREACT    ; save this reaction

SOFT1

JSR     LEFTRIGHT       ; do we have a preference left or right

CMPB    #REACTLEFT      ; if we need to go left, go left

BEQ     SOFTL           ; go left

#ifdef __PRINTOBJAVOID2_

PSHX                    ; save reg X

LDX     #RSOFTSTR       ; print soft right string

JSR     OUTSTR          ;

PULX                    ; restore reg X

#endif

SOFTR       LDX     #SOFTRIGHT      ; go soft right

JSR     STEER           ;

JMP     OBJAVOIDX       ; get out

SOFTL

#ifdef __PRINTOBJAVOID2_

PSHX                    ; save reg X

LDX     #LSOFTSTR       ; print soft left string

JSR     OUTSTR          ;

PULX                    ; restore reg X

#endif

LDX     #SOFTLEFT       ; go soft left

JSR     STEER           ;

JMP     OBJAVOIDX       ; get out

*

*******************************************************************************

* Filename      : FOLLOW.ASM

* Programmer    : Michael Hattermann

* Date          : March 31, 2002

* Version       : 1.0

* Description   : This file contains the code for

*                 object following. The following

*                 functions are available:

*

*

*

*#define __DEBUGFOLLOW_ 1

*#define __PRINTFOLLOW_  1

#include "hc12.asm"

*

************************************************************

* Object Following Equates

************************************************************

*

MINFOLLOW       EQU     $55         ; minimum reading on sensor to execute following

OBJAVOIDSPD     EQU     HALFSPEED   ; speed to perform object avoidance at

MINFOLLOWSPD    EQU     HALFSPEED   ; minimum speed to follow at

MAXFOLLOWSPD    EQU     FULLSPEED   ; maximum speed to follow at

FOLLOWTURNSPD   EQU     _5_8_SPEED  ; max speed to perform a hard turn at

NUMAVGCNT       EQU     20          ; number of sensor values to average

SPDACCEL        EQU     1           ; desired amount of acceleration

SPDDOWNACCEL    EQU     -2          ; slow down acceleration

SPDUPACCEL      EQU     2           ; speed up acceleration

*

************************************************************

* Object Following Debug Code

************************************************************

*

#ifdef __DEBUGFOLLOW_

ORG     USERPROG_PVECT

JMP     TEST

ORG     $B000

TEST        LDAA    #$00            ; turn off COP watchdog timer

STAA    COPCTL

LDS     #$0bff          ; init the stack pointer

HERE        BRA     HERE            ; end of test program

CFVALUE     DC.B    $00             ; center follow sensor value

LFVALUE     DC.B    $00             ; left follow sensor value

RFVALUE     DC.B    $00             ; right follow sensor value

FTBLIDX     DC.B    $00             ; index into reaction table

LASTFOLLOW  DC.B    $00             ; last follow direction

OLDCFAVG    DC.W    $0000           ; old average of center follow sensor values

NEWCFAVG    DC.W    $0000           ; new average of center follow sensor values

AVGCNT      DC.B    $0000           ; number of items in new average

#include "atd.asm"

#include "pwm.asm"

#endif

* Reaction table for following        (Center|Left|Right)

************************************************************

FOLLOWTBL   DC.W    FOBJAVOID       ; 000 - Object avoidance

DC.W    FHARDR          ; 001 - Hard right

DC.W    FHARDL          ; 010 - Hard left

DC.W    FCONT           ; 011 - ERROR - do what we did last

DC.W    FFOWARD         ; 100 - Foward

DC.W    FSOFTR          ; 101 - Soft right

DC.W    FSOFTL          ; 110 - Soft left

DC.W    FCONT           ; 111 - ERROR - do what we did last

*

*******************************************************************************

*                       SUBROUTINE -  FOLLOW

* Description: Performs obstacle following behavior by reading the values

*               from the IR sensors and moving the robot accordingly.

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

FOLLOW      PSHX                        ; save register X

PSHD                        ; save register D

*            JSR     BUMPED              ; check to see if we bumped something

*            TBEQ    A,FOLLOW1           ; no bump, continue following behavior

*            JMP     MAINOUT             ; we bumped something, quit program

FOLLOW1     JSR     FGETDATA            ; get data from following sensors

#ifdef __PRINTFOLLOW_

PSHD                        ; save reg D

PSHX                        ; save reg X

LDAA    LFVALUE             ; print left value

JSR     OUTNUM

LDAA    #$20                ; print space

JSR     OUTCHAR

LDAA    CFVALUE             ; print center value

JSR     OUTNUM

LDAA    #$20                ; print space

JSR     OUTCHAR

LDAA    RFVALUE             ; print right value

JSR     OUTNUM

LDX     #NEWLINE            ; print new line

JSR     OUTSTR

PULX                        ; restore reg X

PULD                        ; restore reg D

#endif

FOLLOW2

LDX     #FOLLOWTBL          ; load address of reaction table

LDAA    FTBLIDX             ; get the reaction table index

LSLA                        ; convert to 16-bit index

LDX     A,X                 ; get address of handling routine

JMP     0,X                 ; jump to appropriate routine

FOLLOWX     PULD                        ; restore register D

PULX                        ; restore register X

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINE -  FGETDATA

* Description: Reads the values from the following IR detectors.

* Input         : None.

* Output        : LFVALUE,RFVALUE.

* Destroys      : LFVALUE,RFVALUE.

* Calls         : None.

*******************************************************************************

*

FGETDATA    PSHA                        ; save register A

MOVB    #$00,FTBLIDX        ; clear reaction table index

LDAA    #CENTERFOLLOW       ; get data from center sensor

JSR     ANALOG              ;

STAA    CFVALUE             ; save center sensor value

CMPA    #MINFOLLOW          ; did center see speeding car?

BLO     FGETDATA1           ; no, so continue

BSET    FTBLIDX,BIT2        ; yes, so set bit in index

FGETDATA1   LDAA    #LEFTFOLLOW         ; get data from left sensor

JSR     ANALOG              ;

STAA    LFVALUE             ; save left sensor value

CMPA    #MINFOLLOW          ; did left see speeding car?

BLO     FGETDATA2           ; no, so continue

BSET    FTBLIDX,BIT1        ; yes, so set bit in index

FGETDATA2   LDAA    #RIGHTFOLLOW        ; get data from right sensor

JSR     ANALOG              ;

STAA    RFVALUE             ; save right sensor value

CMPA    #MINFOLLOW          ; did right see speeding car?

BLO     FGETDATAX           ; no, so get out

BSET    FTBLIDX,BIT0        ; yes, so set bit in index

FGETDATAX   PULA                        ; restore register A

RTS                         ; return to caller

*

*******************************************************************************

*                       SUBROUTINES -  FHARDR,FHARDL,FFOWARD,FSOFTR,FSOFTL,FCONT

* Description: Handle motor control for following behavior

* Input         : None.

* Output        : None.

* Destroys      : Reg X, Reg D.

* Calls         : STEER.

*******************************************************************************

*

FHARDR      MOVB    FTBLIDX,LASTFOLLOW  ; save off last table index

LDD     #FOLLOWTURNSPD      ; set speed to turning speed

JSR     CHNGSPEED           ;

LDX     #HARDRIGHT          ; turn hard right

JSR     STEER               ;

JMP     FOLLOWX             ; get out

FHARDL      MOVB    FTBLIDX,LASTFOLLOW  ; save off last table index

LDD     #FOLLOWTURNSPD      ; set speed to turning speed

JSR     CHNGSPEED           ;

LDX     #HARDLEFT           ; turn hard left

JSR     STEER               ;

JMP     FOLLOWX             ; get out

FFOWARD     MOVB    FTBLIDX,LASTFOLLOW  ; save off last table index

JSR     SPEEDCALC           ; go set new speed

LDX     #GOFOWARD           ; go foward

JSR     STEER               ;

JMP     FOLLOWX             ; get out

FSOFTR      MOVB    FTBLIDX,LASTFOLLOW  ; save off last table index

JSR     SPEEDCALC           ; go set new speed

LDX     #SOFTRIGHT          ; turn soft right

JSR     STEER               ;

JMP     FOLLOWX             ; get out

FSOFTL      MOVB    FTBLIDX,LASTFOLLOW  ; save off last table index

JSR     SPEEDCALC           ; go set new speed

LDX     #SOFTLEFT           ; turn soft left

JSR     STEER               ;

JMP     FOLLOWX             ; get out

FCONT       LDX     #FOLLOWTBL          ; load address of reaction table

LDAA    LASTFOLLOW          ; get the last reaction index

STAA    FTBLIDX             ; save as current reaction

LSLA                        ; convert to 16-bit index

LDX     A,X                 ; get address of handling routine

JMP     0,X                 ; jump to appropriate routine

*

*******************************************************************************

*                       SUBROUTINE -  FOBJAVOID

* Description: Handles object avoidance for following behavior

* Input         : None.

* Output        : None.

* Destroys      : Reg X, Reg D.

* Calls         : SIRENON,SIRENOFF,OBJAVOID,WAIT.

*******************************************************************************

*

FOBJAVOID   JSR     SIRENOFF            ; turn off siren to indicate we lost speeder

LDD     #OBJAVOIDSPD        ; set motor speed to obj avoid speed

JSR     CHNGSPEED           ;

FOBJAVOID1  JSR     OBJAVOID            ; avoid obstacles

LDX     #OAPROCRATE         ; wait designated amount of time

JSR     WAIT                ;

JSR     FGETDATA            ; check following sensors

TST     FTBLIDX             ; did we find the speeder?

BEQ     FOBJAVOID1          ; no, continue object avoidance

JSR     SIRENON             ; turn siren on to indicate active chase

LDX     #FOLLOWTBL          ; load address of reaction table

LDAA    FTBLIDX             ; get the reaction table index

LSLA                        ; convert to 16-bit index

LDX     A,X                 ; get address of handling routine

JMP     0,X                 ; jump to appropriate routine

*

*******************************************************************************

*                       SUBROUTINE -  SPEEDCALC

* Description: Calculates and sets the next max motor speed so that the robot

*               has a constant acceleration

* Input         : None.

* Output        : None.

* Destroys      : Reg X, Reg D.

* Calls         : .

*******************************************************************************

*

SPEEDCALC   LDD     NEWCFAVG            ; load the current working average

ADDB    CFVALUE             ; add the newest center sensor

ADCA    #$00                ; to the current average

LDX     AVGCNT              ; get the count of # items in working average

INX                         ; increment the count

STX     AVGCNT              ; save the count

CPX     #NUMAVGCNT          ; do we have the correct sum yet?

BLT     SPEEDCALCX          ; no, get out

IDIVS                       ; calculate average

XGDX                        ; get average

STD     NEWCFAVG            ; save average

#ifdef __PRINTFOLLOW_

PSHX                        ; save reg X

LDX     OLDCFAVG            ; print old average

JSR     OUTADDR             ;

LDAA    #$20                ; print a space

JSR     OUTCHAR             ;

LDX     NEWCFAVG            ; print new average

JSR     OUTADDR             ;

LDX     #NEWLINE            ; print newline

JSR     OUTSTR              ;

PULX                        ; restore reg X

#endif

SUBD    OLDCFAVG            ; calc difference between old,new average

CPD     #SPDACCEL           ; compare to the desired acceleration

BEQ     SPEEDCALC4          ; they are equal, do nothing

BLT     SPEEDCALC2          ; need to speed up

* SLOW DOWN

LDD     MAXFOWARDSPD        ; get the current max speed

ADDD    #SPDDOWNACCEL       ; slow it down

CPD     #MINFOLLOWSPD       ; have we slowed down too far?

BGE     SPEEDCALC1          ; no, skip adjustment

LDD     #MINFOLLOWSPD       ; make speed = minimum speed

SPEEDCALC1  JSR     CHNGSPEED           ; set the new speed

BRA     SPEEDCALC4          ; get out

* SPEED UP

SPEEDCALC2  LDD     MAXFOWARDSPD        ; get the current max speed

ADDD    #SPDUPACCEL         ; speed it up

CPD     #MAXFOLLOWSPD       ; have we speed up too far?

BLE     SPEEDCALC3          ; no, skip adjustment

LDD     #MAXFOLLOWSPD       ; make speed = maximum speed

SPEEDCALC3  JSR     CHNGSPEED           ; set the new speed

SPEEDCALC4  MOVW    NEWCFAVG,OLDCFAVG   ; make new average the old average

MOVW    #$0000, NEWCFAVG    ; clear new average to start over

MOVW    #$0000,AVGCNT       ; clear average count for next time

SPEEDCALCX  RTS                         ; return to caller

*

*******************************************************************************

* Filename      : MAIN.ASM

* Programmer    : Michael Hattermann

* Date          : February 22, 2002

* Version       : 1.0

* Description   : This file contains the main routine to

*                   control the rest of the robot.  It

*                   includes all the other control files.

*                   The followong functions are available:

*

*                   MAIN - start of program, inits/uses systems

*                   MAINOUT - end of program, kills systems

*

#include "hc12.asm"

*

************************************************************

* Main Equates

************************************************************

*

PROGSTART       EQU         $B000       ; start of the program

STACKPTR        EQU         $0A00       ; bottom of internal RAM for stack

GLBLVARS        EQU         $0900       ; top of internal RAM for global variables

OAPROCRATE      EQU         10          ; how often to execute object avoidance (in ms)

FPROCRATE       EQU         10          ; how often to execute following (in ms)

*

************************************************************

* Global Variables

************************************************************

*

ORG     GLBLVARS

UPPERTIMER      DC.W    $0000           ; 16-bit extension of TCNT

LEFTSPDTIME     DC.W    $0000           ; Time left break beam was broken

RIGHTSPDTIME    DC.W    $0000           ; Time right break beam was broken

SPDTIMEFLG      DC.B    $00             ; Flags to indicate which beams were broken

SPDCAUGHT       DC.B    $00             ; Flags to indicate speeder caught

FLASHTIMER      DC.B    $00             ; Timer for flashing lights

FLASHPREV       DC.B    $00             ; Previous status of lights

SIRENFREQ       DC.W    $0000           ; Frequency of the siren

SIRENTIMER      DC.W    $0000           ; Timer for siren

OLEFTSPD        DC.W    $0000           ; current speed of left motor

NLEFTSPD        DC.W    $0000           ; next speed of left motor

ORIGHTSPD       DC.W    $0000           ; current speed of right motor

NRIGHTSPD       DC.W    $0000           ; next speed of right motor

MAXFOWARDSPD    DC.W    $0000           ; maximum foward speed for motors

MAXBACKSPD      DC.W    $0000           ; maximum reverse speed for motors

LVALUE          DC.B    $00             ; value of left IR

LREACT          DC.B    $00             ; reaction to left IR value

RVALUE          DC.B    $00             ; value of right IR

RREACT          DC.B    $00             ; reaction to right IR value

CVALUE          DC.B    $00             ; value of center IR

CREACT          DC.B    $00             ; reaction to center IR value

PREVRAND        DC.B    $00             ; previous random turning direction

PREVREACT       DC.B    $00             ; previous reaction value

CURRMAN         DC.W    $0000           ; current manuever being performed

LFVALUE         DC.B    $00             ; left follow sensor value

CFVALUE         DC.B    $00             ; center follow sensor value

RFVALUE         DC.B    $00             ; right follow sensor value

FTBLIDX         DC.B    $00             ; index into reaction table

LASTFOLLOW      DC.B    $00             ; last follow direction

OLDCFAVG        DC.W    $0000           ; old average of center follow sensor values

NEWCFAVG        DC.W    $0000           ; new average of center follow sensor values

AVGCNT          DC.B    $0000           ; number of items in new average

BUMPVALUE       DC.B    $00             ; A/D bumper value from wait function

*

************************************************************

* Pseudointerrupt vectors

************************************************************

*

ORG     T0_PVECT

JMP     LEFTSTS

ORG     T1_PVECT

JMP     RIGHTSTS

ORG     TMR_OVER_PVECT

JMP     TIMEEXT

ORG     RTI_PVECT

JMP     UPDMOTORS

ORG     T6_PVECT

JMP     SIREN

ORG     USERPROG_PVECT

JMP     MAIN

ORG     PROGSTART

*

************************************************************

* Main Constants

************************************************************

*

WELCOME     DC.B    CR,LF

DC.B    'STEVE - Speed Trap Enforcement VehiclE'

DC.B    CR,LF

DC.B    'Michael Hattermann'

DC.B    CR,LF

DC.B    'IMDL - Spring 2002'

DC.B    CR,LF,EOS

SHUTDOWN    DC.B    CR,LF

DC.B    'STEVE - Program ended...shutting down systems'

DC.B    CR,LF,EOS

LEFTIRSTR   DC.B    'Left IR value = '

DC.B    EOS

RIGHTIRSTR  DC.B    'Right IR value = '

DC.B    EOS

NEWLINE     DC.B    CR,LF,EOS

LEFTSPSTR   DC.B    'Left beam broken'

DC.B    CR,LF,EOS

RIGHTSPSTR  DC.B    'Right beam broken'

DC.B    CR,LF,EOS

SPEED       DC.B    CR,LF

DC.B    'SPEED = '

DC.B    EOS

*

*******************************************************************************

*                       SUBROUTINE -  MAIN

* Description: Main program.  Inits the robots sub-systems and begins the robot

*               behavior code.

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : None.

*******************************************************************************

*

MAIN        MOVB    #$00,COPCTL         ; turn off COP watchdog timer

LDS     #STACKPTR           ; load stack pointer

JSR     INITSCI             ; init SCI system

JSR     INITATD             ; init A/D system

JSR     INITTIME            ; init timer system

MOVB    #$00,LED1PORT       ; turn off flashing lights

MOVB    #$00,SEG7PORT       ; reset speed capture to zero

LDX     #WELCOME            ; print welcome message

JSR     OUTSTR              ;

CLI                         ; turn on interrupts

JSR     WAITSPEED           ; wait for a speeder

JSR     INITPWM             ; init PWM system

JSR     FLASHON             ; turn on flashing lights

JSR     SIRENON             ; turn on siren

JSR     PULLOUT             ; pull out and prepare to follow

MAIN2

JSR     FOLLOW              ; follow speeder

LDX     #FPROCRATE          ; wait designated amount of time

JSR     WAIT                ;

BRA     MAIN2               ; do it again

*

*******************************************************************************

*                       SUBROUTINE -  MAINOUT

* Description: Exits the program.  Stops motors, signals end of program with

*               the lights, then shuts down the subsystems and enters a

*               never ending loop

* Input         : None.

* Output        : None.

* Destroys      : None.

* Calls         : STEER,OUTSTR,WAIT,KILLATD,KILLPWM,KILLTIME.

*******************************************************************************

*

MAINOUT     LDX     #STOP               ; stop the motors

JSR     STEER               ;

LDX     #SHUTDOWN           ; print shutdown message

JSR     OUTSTR              ;

LDAA    #8                  ; load loop counter

MAINOUT1    MOVB    #$3C,LED1PORT       ; turn off lights

JSR     SIRENOFF            ; turn off siren

LDX     #250                ; wait

JSR     WAIT                ;

MOVB    #$C3,LED1PORT       ; turn on lights

JSR     SIRENON             ; turn on siren

LDX     #250                ; wait

JSR     WAIT                ;

DBNE    A,MAINOUT1          ; continue looping until done

MOVB    #$00,LED1PORT       ; turn on lights

JSR     KILLATD             ; shutdown atd system

JSR     KILLPWM             ; shutdown pwm system

JSR     KILLTIME            ; shutdown timer system

MOVB    #$00,LED1PORT       ; turn off flashing lights

MOVB    #$00,SEG7PORT       ; clear 7 segment display

MAINOUTX    BRA     MAINOUTX            ; end of program

*

*******************************************************************************

#include "wait.asm"

#include "sci.asm"

#include "atd.asm"

#include "time.asm"

#include "pwm.asm"

#include "objavoid2.asm"

#include "follow.asm"